## Slide 1
NETWORK INFRASTRUCTURE WORKSHOP · SOMNOG9
Introduction to Networks
Components, Media, Protocols and the Layered Models
Track 1 — Network Infrastructure · SNU KM4 Campus, Mogadishu

## Slide 2
LEARNING OBJECTIVES
By the End of This Session
Name the three parts of any network — devices, media and services — and give an example of each
Tell the difference between a LAN, a WAN and the Internet, and say which one you are using
Choose the right cable for a job, and explain why copper stops at about 100 metres
Explain what a protocol is, and why the industry agrees on standards
Follow one message down the OSI and TCP/IP layers and name what it is called at each step
Learning Objectives
2

## Slide 3
AGENDA
What We'll Cover
Why networks matter, and the three parts every network is built from
Network types — LAN, WAN, the Internet, intranet and extranet
Network media — copper, fibre and wireless, and how to test each one
Rules of communication — protocols, standards, and who writes them
Reference models — OSI, TCP/IP, and how data is encapsulated
Agenda
3

## Slide 4
IN TODAY’S LAB
From Concept to Console
You will cable your own pod — two switches and one router per group of five
You will make and test your own UTP patch cable, then use it for real in the rack
You will connect by console cable and do the basic housekeeping on a live switch
Everything after this session — VLANs, trunks, routing — runs over the cabling you build today
A cable that passes a tester still fails if it is too long. Keep every copper run under 100 metres, patch cords included.
In Today's Lab
4

## Slide 5
WHY IT MATTERS
Networks Carry Everything We Do
Networks carry how we learn — online classes, research, and shared libraries
Networks carry how we communicate — voice, messaging, video and email
Networks carry how we work — banking, mobile money, logistics and government services
Networks carry how we play — streaming, gaming and social media
Connected devices keep climbing: 18.5 billion in 2024 and 21.1 billion by the end of 2025, forecast to reach 39 billion by 2030 (IoT Analytics)
Introduction
5

## Slide 6
THE EVOLUTION
Share of the World Online, 2005–2025
16%
2005
30%
2010
40%
2015
60%
2020
74%
2025
Percentage of the world population using the Internet. Source: ITU, Facts and Figures 2025.
About 6.0 billion people are online in 2025 — 1.3 billion of them came online in the last five years alone.
Introduction
6

## Slide 7
WHERE WE STAND
Connectivity in 2026
74%
of the world uses the Internet — about 6.0 billion people, up from 60% in 2020
2.2bn
are still offline. 96% of them live in low- and middle-income countries
36%
is the figure for Africa — the lowest of any ITU region, against 94% in high-income countries
55%
of the world population is now covered by 5G, but only 4% in low-income countries
Source: ITU, Facts and Figures 2025 (published November 2025). Somalia estimates range from about 28% (ITU method) to 55% (Kepios/DataReportal), depending on how a user is counted.
Introduction
7

## Slide 8
COMPONENTS
Every Network Has Three Parts
Devices
The things that send, receive or move data
End devices: PCs, phones, servers, printers
Intermediary devices: switches, routers, firewalls, access points
Media
The path the signal travels along
Copper carries electrical signals
Fibre carries pulses of light
Wireless carries radio waves
Services
The software that gives the network a purpose
Email, web, file sharing, DNS, DHCP
Without services, a network just moves bits nobody uses
Components of a Network
8

## Slide 9
DEVICE ROLES
End Devices and Intermediary Devices
End Devices
Where a message starts or finishes
Laptops, desktops, phones, tablets, IP phones, servers, printers, cameras and sensors
Each one needs an address so the network can find it
Also called hosts
Intermediary Devices
Everything in between that carries the message along
Switches connect devices inside one network
Routers connect different networks together
Firewalls and access points also sit in this group
They make forwarding decisions; they are not the source or the destination
Components of a Network
9

## Slide 10
NETWORK TYPES
Networks Are Named by How Far They Reach
LAN
Local Area Network
One home, one building, one campus
Owned and managed by one organisation
Usually high speed and low delay
WAN
Wide Area Network
Joins LANs that are far apart
Almost always uses links rented from a service provider
Usually slower and more costly per megabit than a LAN
Others You Will Meet
MAN — covers a city
WLAN — a LAN using Wi-Fi instead of cable
PAN — a few metres, e.g. Bluetooth
SAN — a network built for storage traffic
Types of Networks
10

## Slide 11
SCOPE AND ACCESS
Internet, Intranet and Extranet
The Internet
A worldwide mesh of networks that agreed to interconnect
No single owner — it works because everyone uses the same protocols
Open to the public
Intranet
A private network for one organisation only
Staff can reach it; outsiders cannot
Uses the same technology as the Internet, but kept closed
Extranet
A controlled opening in the intranet
Lets named suppliers, customers or partners reach agreed resources
Access is granted, logged and can be withdrawn
Types of Networks
11

## Slide 12
ACCESS
How Users Reach the Internet
Fibre to the home (FTTH/GPON) — the fastest fixed option, and the one most new builds now use
Fixed wireless — a radio link from an ISP tower to an antenna on the roof; common where trenching fibre is hard
Mobile broadband — 4G LTE and 5G; in much of Africa this is how most people first reach the Internet
Satellite — traditional geostationary service, and newer low-earth-orbit systems with far lower delay
Cable and DSL — older copper-based services, still in use but being retired in many markets
Connecting to the Internet
12

## Slide 13
CHECK YOUR UNDERSTANDING
Checkpoint 1 — Network Basics
QUESTION 1
Which of these is an intermediary device?
A. A laptop
B. A network printer
C. A switch
D. An IP camera
QUESTION 2
Two offices in different cities are joined by a link rented from an ISP. What is that?
A. A LAN
B. A WAN
C. A PAN
D. An intranet
QUESTION 3
What best describes an extranet?
A. A private network for staff only
B. A controlled part of a private network opened to named partners
C. The public Internet
D. A wireless LAN
Checkpoint
13

## Slide 14
MEDIA
Three Ways to Carry a Signal
Copper
Carries electrical signals along metal wires
Cheap, easy to terminate, widely available
Limited to about 100 m and affected by electrical noise
Fibre
Carries pulses of light along a glass core
Very long distances and very high bandwidth
Completely immune to electrical interference
Costs more and needs more skill to install
Wireless
Carries radio waves through the air
No cable to pull — the only choice for mobile devices
Shared medium: coverage, interference and security all need planning
Network Media
14

## Slide 15
COPPER MEDIA
The Copper Cables You Will Handle
UTP
Unshielded Twisted Pair
Four pairs, twisted to cancel out interference
The standard cable for LANs and for this workshop
Terminated with an RJ-45 plug
STP
Shielded Twisted Pair
UTP plus a metal shield around the pairs
Used near motors, generators or heavy power cable
Costs more, is stiffer, and the shield must be earthed to work
Coaxial
One centre conductor inside a braided shield
No longer used for Ethernet LANs
Still seen on cable broadband and on antenna feeds
Copper Cabling
15

## Slide 16
STANDARDS
UTP Categories — What to Buy Today
Cat5e — supports 1 Gbps to 100 m. The old minimum; fine for existing runs, but not what you would install now
Cat6 — supports 1 Gbps to 100 m and 10 Gbps up to about 55 m. The common choice for new office cabling
Cat6a — supports 10 Gbps to the full 100 m. Use it for links between floors and to access switches
Cat7 and Cat8 — shielded, for short high-speed runs inside data centres; rarely worth it in a campus
Cat3 and Cat5 appear in old buildings and in old slide decks — treat them as things to replace, not to install
The category is only as good as the weakest part. A Cat6a run patched with a Cat5e cord performs like Cat5e.
Copper Cabling
16

## Slide 17
WIRING
Straight-Through, Crossover and Rollover
Straight-Through
Same standard on both ends — T568A to T568A, or T568B to T568B
Connects a host to a switch or router
The cable you will make and use most often
Crossover
T568A on one end, T568B on the other
Connects two devices of the same kind — switch to switch, or PC to PC
Swaps the transmit and receive pairs
Rollover
Cisco-specific; the pin order is fully reversed
Connects a PC to a router or switch console port
This is the light blue cable in your kit
Modern switches use Auto-MDIX and fix the crossing themselves, so a straight-through cable usually works switch-to-switch. Know the rule anyway — older kit does not.
Copper Cabling
17

## Slide 18
VERIFICATION
Testing a Copper Cable
Wire map — is every pin at one end connected to the right pin at the other end?
Length — is the run inside the 100 m limit, patch cords included?
Attenuation — how much signal is lost along the way
Crosstalk — how much one pair interferes with its neighbours
A cheap continuity tester finds a bad crimp; only a certification tester proves the link meets its category
Copper Cabling
18

## Slide 19
FIBRE MEDIA
Single-Mode and Multimode Fibre
Single-Mode
Core about 9 microns — light takes one straight path
Driven by a laser
Reaches tens of kilometres
Used for long haul, between sites, and for submarine cable
Multimode
Core 50 or 62.5 microns — light takes several paths
Driven by an LED or VCSEL
Reaches a few hundred metres
Used inside a building, in data centres, and between nearby buildings
Both types use 125-micron cladding, so the cables look identical. Always check the jacket marking before you patch.
Fibre Optic Cabling
19

## Slide 20
FIBRE MEDIA
Connectors, Testing and Care
LC is the connector you will see most — small, latching, usually in duplex pairs
SC and ST are older and larger; MPO carries twelve or more fibres in one connector for high-speed links
An optical power meter tells you how much light is arriving — the first thing to check on a dark link
An OTDR tells you where a break or a bad splice is along the cable, measured in metres from your end
Most fibre faults are dirty connectors. Clean before you plug in, and cap every port you are not using
Fibre Optic Cabling
20

## Slide 21
COMPARISON
Fibre Versus Copper
Where Copper Wins
Lower cost for cable, connectors and tools
Easier to terminate — you can learn it in an afternoon
Can carry power to a device with PoE, which fibre cannot
Good enough for any run under 100 m
Where Fibre Wins
Distance — hundreds of metres to hundreds of kilometres
Bandwidth — comfortably 100 Gbps and beyond
Completely immune to electrical noise and lightning surges
No electrical path between buildings, which protects your equipment
Network Media
21

## Slide 22
WIRELESS MEDIA
Wi-Fi and Other Radio Standards
Wi-Fi is IEEE 802.11. Devices share the air using CSMA/CA — they listen first and avoid talking over each other
Wi-Fi 4 (802.11n) and Wi-Fi 5 (802.11ac) are the older generations still common in deployed networks
Wi-Fi 6 and 6E (802.11ax) added efficiency in crowded places and opened the 6 GHz band
Wi-Fi 7 (802.11be) was published in July 2025 and is the current generation — 320 MHz channels and multi-link operation across bands
Wi-Fi 8 (802.11bn) is still a draft, due about 2028. It targets reliability and roaming rather than a higher top speed
Bluetooth (802.15) pairs devices over short distances; 5G fixed wireless has largely replaced WiMAX for broadband access
Wireless is a shared medium. Every extra user on a channel takes a share of the same airtime — coverage, interference and security all need planning.
Wireless Media
22

## Slide 23
CHECK YOUR UNDERSTANDING
Checkpoint 2 — Media & Cabling
QUESTION 4
Auto-MDIX is switched off. Which cable joins two switches?
A. Straight-through
B. Crossover
C. Rollover
D. Coaxial
QUESTION 5
Which fibre gives light a single path and reaches furthest?
A. Multimode
B. Single-mode
C. Coaxial
D. Shielded twisted pair
QUESTION 6
A link between two buildings must run 180 m. What do you do?
A. Use Cat6a — it reaches 180 m
B. Use fibre — copper Ethernet stops at about 100 m
C. Join two cables with a coupler
D. Use a rollover cable
Checkpoint
23

## Slide 24
THE RULES
Protocols and Standards
A Protocol
An agreed set of rules for a conversation
Fixes how a message is formatted, how devices share what they know, how errors are reported, and how a session starts and ends
People use protocols too — one language, take turns, signal when finished
A Standard
A protocol that an industry body has reviewed and published
It means equipment from different vendors will work together
Open standards are why a Cisco switch talks to a Juniper router, and why the Internet could grow at all
Protocols and Communication
24

## Slide 25
WHO SETS THE RULES
Standards Organisations
IETF — writes the protocols of the Internet and publishes them as RFCs; anyone may take part
IEEE — defines the physical and data link standards: 802.3 Ethernet, 802.11 Wi-Fi, 802.1Q VLANs
ISO — publishes the OSI reference model used to describe how layers fit together
ICANN and IANA — look after names and numbers: domain names, IP address blocks, protocol numbers
ITU-T, TIA and EIA — cover telecom and structured cabling, including the T568A and T568B pinouts
Standards Organisations
25

## Slide 26
REFERENCE MODELS
The OSI Model — Seven Layers
7 Application — the interface to the user’s program: HTTP, SMTP, DNS
6 Presentation — formats the data: coding, compression, encryption
5 Session — starts, keeps and restarts the dialogue between two programs
4 Transport — splits data into pieces, tracks them, and identifies the application: TCP, UDP
3 Network — addresses and routes packets between networks: IP, and protocols like OSPF
2 Data Link — frames data for one hop across one medium; split into LLC and MAC sublayers
1 Physical — turns bits into signals on copper, fibre or radio
Reference Models
26

## Slide 27
REFERENCE MODELS
The TCP/IP Model — Four Layers
Application — presents data to the user and handles encoding and dialogue. Covers OSI layers 5, 6 and 7
Transport — supports communication between programs on different hosts: TCP and UDP
Internet — finds the best path through the network: IP, ICMP, and the routing protocols
Network Access — controls the hardware and the media that carry the bits. Covers OSI layers 1 and 2
This is the model the Internet actually runs on; OSI is the model used to teach and to describe it
Reference Models
27

## Slide 28
REFERENCE MODELS
Comparing the Two Models
What Is the Same
Both split the work into layers, each with one clear job
Both let a layer be changed without rewriting the ones above and below
Transport and Network line up almost exactly between the two
What Is Different
OSI has seven layers; TCP/IP has four
TCP/IP folds OSI layers 5, 6 and 7 into one Application layer
TCP/IP folds OSI layers 1 and 2 into one Network Access layer
OSI was designed first as a model; TCP/IP grew from working code
Reference Models
28

## Slide 29
ENCAPSULATION
One Message, Five Names
As data moves down the stack, each layer adds its own header. That is encapsulation
At the Application layer the unit is simply data
The Transport layer adds ports and sequence numbers — now it is a segment
The Network layer adds source and destination IP addresses — now it is a packet
The Data Link layer adds MAC addresses and a trailer — now it is a frame
The Physical layer sends it as bits. The receiver strips each header in turn — decapsulation
Reference Models
29

## Slide 30
ASSESSMENT
How You'll Be Assessed
Each lab step is verified before the group moves on — the instructor checks your result against the expected one
Your cable is tested in front of you: wire map first, then it goes into the rack and has to pass traffic
When something does not work, a correct diagnosis counts for as much as a correct answer
Checkpoint questions between sections are formative, not graded — they show where to slow down
Success criteria — by the close of this session each group has a working patch cable of its own making, console access to both switches, and can name the three parts of their pod and the media joining them.
Assessment
30

## Slide 31
SUMMARY
Key Takeaways
Every network is devices, media and services — if you can name all three, you can describe any network
Networks are classified by reach: LAN, WAN, and the Internet that joins them
Copper is cheap and simple but stops at 100 m; fibre goes far and fast; wireless trades certainty for mobility
Protocols are the rules, and open standards are why equipment from different vendors works together
Layered models let you find a fault fast: work up from the cable, or down from the application
Summary
31

## Slide 32
INSTRUCTOR NOTES
Answer Key
Question 1 C
A switch carries traffic between other devices. The rest are end devices — sources or destinations.
Question 2 B
A link between distant sites, rented from a provider, is by definition a WAN.
Question 3 B
An extranet opens a controlled slice of the private network to named outside partners.
Question 4 B
Two devices of the same kind need the transmit and receive pairs swapped — that is a crossover.
Question 5 B
The 9-micron core of single-mode gives light one path, so it travels tens of kilometres.
Question 6 B
Copper Ethernet is limited to about 100 m regardless of category. Past that, use fibre.
Answer Key — remove for student handout
32

## Slide 33
Questions?
Introduction to Networks — Network Infrastructure Workshop, SomNOG9
Based on original materials by the Network Startup Resource Center (NSRC, nsrc.org)
Licensed under Creative Commons Attribution-NonCommercial 4.0 International