## Slide 1
NETWORK INFRASTRUCTURE WORKSHOP · SOMNOG9
IP Addressing & Subnetting
Addressing, Subnet Masks, CIDR and VLSM
Track 1 — Network Infrastructure · SNU KM4 Campus, Mogadishu

## Slide 2
LEARNING OBJECTIVES
By the End of This Session
Read an IPv4 address in both dotted-decimal and binary, and convert between the two
Spot an invalid address on sight — and say exactly which rule it breaks
Explain what a subnet mask does, and read a prefix such as /26 without a calculator
Work out the network ID, first host, last host and broadcast address for any subnet
Apply VLSM to give each segment only the addresses it needs, largest segment first
Learning Objectives
2

## Slide 3
AGENDA
What We'll Cover
IP addressing — the 32 bits, the four octets, and the rules an address must obey
Subnet masks and prefix length — where the network part ends and the host part begins
Subnetting — splitting one network into many, with worked examples
CIDR — why classes were abandoned and how the Internet is addressed today
VLSM — right-sizing every subnet so you stop wasting addresses
Agenda
3

## Slide 4
IN TODAY’S LAB
From Concept to Console
Your pod uses a fixed scheme: the second octet is always your group ID, so group 3 works inside 10.3.0.0
VLAN 100 and VLAN 200 each get their own subnet, and each gets its own DHCP pool
The link to your peer group is a point-to-point WAN link — a /30, two usable addresses, nothing wasted
You will assign these by hand before OSPF ever runs, so an addressing mistake shows up as a failed ping
Every later lab — DHCP, inter-VLAN routing, static routes, OSPF, NAT — is built on the addressing you get right today.
In Today's Lab
4

## Slide 5
FUNDAMENTALS
What an IPv4 Address Is
An IPv4 address identifies one interface on an IP network — not a device, an interface
It is 32 bits long, written as four 8-bit octets separated by dots
Each octet is a number from 0 to 255, so 256 values per octet
Part of the address names the network; the rest names the host. The subnet mask draws that line
Written as dotted decimal for humans, for example 172.16.81.100 — the router only ever sees the bits
IP Addressing
5

## Slide 6
FUNDAMENTALS
Reading an Octet in Binary
Each of the eight bit positions has a value: 128, 64, 32, 16, 8, 4, 2, 1
To convert binary to decimal, add the values of every position holding a 1
10000000 is 128. 11000000 is 128 + 64 = 192. 11111111 is 255
To convert decimal to binary, subtract the largest value that fits, then work down the row
Learn the eight numbers and every subnetting question becomes arithmetic you can do on paper
128 64 32 16 8 4 2 1 — write this row at the top of your page before you start any subnetting exercise.
IP Addressing
6

## Slide 7
WORKED EXAMPLE
Binary to Dotted Decimal
QUESTION
Convert this address to dotted-decimal notation:
10000001 00001011 00001011 11101111
SOLUTION
129.11.11.239
128+1 = 129, 8+2+1 = 11, 8+2+1 = 11, 128+64+32+8+4+2+1 = 239
Worked Example
7

## Slide 8
WORKED EXAMPLE
Dotted Decimal to Binary
QUESTION
Convert this address to binary notation:
111.56.45.78
SOLUTION
01101111 00111000 00101101 01001110
111 = 64+32+8+4+2+1, 56 = 32+16+8, 45 = 32+8+4+1, 78 = 64+8+4+2
Worked Example
8

## Slide 9
FIND THE ERROR
Is This a Valid Address?
QUESTION
Find the error in the following IP address:
111.56.045.78
SOLUTION
Leading zeroes are not written in dotted-decimal notation
045 should be written 45. Some systems read a leading zero as octal, so 045 could even be read as 37.
Find the Error
9

## Slide 10
FIND THE ERROR
Is This a Valid Address?
QUESTION
Find the error in the following IP address:
75.45.301.14
SOLUTION
Each octet is 8 bits, so the largest value it can hold is 255
301 is out of range. The highest address of all is 255.255.255.255.
Find the Error
10

## Slide 11
MASKS
Subnet Masks and Prefix Length
The mask marks which bits are network. A 1 means network, a 0 means host
255.255.255.0 is 24 ones followed by 8 zeros — so it is written /24
/25 is 255.255.255.128, /26 is 255.255.255.192, /27 is 255.255.255.224, /30 is 255.255.255.252
Host bits give you the size: 2 to the power of the host bits, minus 2 for the network ID and the broadcast
A /24 has 8 host bits, so 256 addresses and 254 usable. A /30 has 2 host bits, so 4 addresses and 2 usable
Subnet Masks
11

## Slide 12
HISTORY
Address Classes — and Why They Went Away
The Classful Scheme
Class A: first octet 1–126, mask 255.0.0.0, 16.7 million hosts
Class B: first octet 128–191, mask 255.255.0.0, 65,534 hosts
Class C: first octet 192–223, mask 255.255.255.0, 254 hosts
Class D (224–239) is multicast; Class E (240–255) is reserved
127.0.0.0/8 is loopback and belongs to no class
Why It Failed
The three sizes fitted almost nobody — an office of 300 staff had to take a Class B and waste 65,000 addresses
CIDR replaced classes in 1993 (RFC 1518 and 1519) and let the prefix fall on any bit boundary
Classes are still worth knowing because old documents and exam questions use the words
No router has made a forwarding decision based on class for over thirty years
When someone says "a class C network" today they usually just mean a /24. The class itself no longer decides anything.
Address Classes
12

## Slide 13
SCOPE
Public and Private Addresses
Public
Globally unique — no two hosts on the Internet may share one
Routable across the Internet
Assigned through IANA and your regional registry, which is AFRINIC for Somalia
Scarce, and increasingly bought and leased rather than granted
Private (RFC 1918)
10.0.0.0/8 — a single large block
172.16.0.0/12 — that is 172.16 through 172.31, not 172.168
192.168.0.0/16
Free to use inside your own network, and every organisation may reuse them
Never routed on the Internet, so NAT translates them on the way out
100.64.0.0/10 (RFC 6598) is a fourth block, reserved for carrier-grade NAT inside ISP networks — do not use it for a campus.
Public and Private
13

## Slide 14
CHECK YOUR UNDERSTANDING
Checkpoint 1 — Addresses and Masks
QUESTION 1
Which of these is not a valid IPv4 address?
A. 172.16.0.1
B. 75.45.301.14
C. 10.255.255.254
D. 192.168.1.255
QUESTION 2
What does the /26 in 192.168.1.0/26 actually tell you?
A. There are 26 hosts
B. The first 26 bits are the network part
C. The mask is 255.255.255.26
D. There are 26 subnets
QUESTION 3
Which of these ranges is private under RFC 1918?
A. 172.168.0.0/12
B. 172.16.0.0/12
C. 192.169.0.0/16
D. 11.0.0.0/8
Checkpoint
14

## Slide 15
SUBNETTING
Why We Subnet
One flat network means one broadcast domain — every broadcast reaches every host
Subnetting splits that address space into smaller networks, each its own broadcast domain
Smaller domains mean less wasted bandwidth and better performance
Boundaries let you apply policy: a guest VLAN can be filtered differently from the finance VLAN
Every separate data link — every VLAN, every WAN link — needs its own network ID
Subnetting
15

## Slide 16
METHOD
The Five Questions
How many subnets does this mask create? Two to the power of the borrowed bits
How many usable hosts per subnet? Two to the power of the host bits, minus two
What are the valid subnets? Count up in the block size, starting at zero
What is the broadcast address of each? The address just before the next subnet starts
What are the valid hosts? Everything between the network ID and the broadcast address
Block size = 256 minus the interesting octet of the mask. For /26 that is 256 − 192 = 64, so subnets land on 0, 64, 128, 192.
Subnetting
16

## Slide 17
WORKED EXAMPLE
192.168.1.0/25 — Two Subnets
Subnet 1
Network ID: 192.168.1.0
First host: 192.168.1.1
Last host: 192.168.1.126
Broadcast: 192.168.1.127
Subnet 2
Network ID: 192.168.1.128
First host: 192.168.1.129
Last host: 192.168.1.254
Broadcast: 192.168.1.255
Mask 255.255.255.128. One bit borrowed, so 2 subnets. Seven host bits, so 2⁷ − 2 = 126 usable hosts in each.
Subnetting
17

## Slide 18
WORKED EXAMPLE
192.168.1.0/26 — Four Subnets
Subnet 1
Network: .0
First: .1
Last: .62
Broadcast: .63
Subnet 2
Network: .64
First: .65
Last: .126
Broadcast: .127
Subnet 3
Network: .128
First: .129
Last: .190
Broadcast: .191
Subnet 4
Network: .192
First: .193
Last: .254
Broadcast: .255
Mask 255.255.255.192. Two bits borrowed, so 4 subnets. Six host bits, so 2⁶ − 2 = 62 usable hosts in each.
Subnetting
18

## Slide 19
PRACTICE
Your Turn — 192.168.1.0/27
QUESTION
What is the mask, how many subnets, and how many usable hosts each?
192.168.1.0/27
SOLUTION
255.255.255.224 — 8 subnets — 30 usable hosts each
Three bits borrowed: 2³ = 8. Five host bits: 2⁵ − 2 = 30. Block size 256 − 224 = 32, so subnets are 0, 32, 64, 96, 128, 160, 192, 224.
Practice
19

## Slide 20
CLASSLESS ROUTING
CIDR
CIDR means Classless Inter-Domain Routing — the prefix may fall on any bit, not just octet boundaries
It let address blocks be sized to the actual need instead of to a class
It also allows aggregation: many small prefixes advertised as one larger prefix
An ISP holding 172.16.0.0/16 can give customers 172.16.1.0/24, 172.16.2.0/24 and so on
To the rest of the Internet the ISP still advertises a single route, 172.16.0.0/16
Aggregation is what keeps the global routing table manageable. Without CIDR the Internet would have run out of both addresses and router memory in the 1990s.
CIDR
20

## Slide 21
VLSM
Fixed-Size Subnets Waste Addresses
Classic subnetting gives every subnet the same mask — fixed length, or FLSM
Real networks are not uniform: one department needs 74 addresses, a WAN link needs 2
With one mask you must size every subnet for the largest segment, and the rest is wasted
Sizing a /25 for a 2-address WAN link wastes 124 addresses on a single cable
VLSM lets each subnet carry its own mask, so each segment gets only what it needs
VLSM
21

## Slide 22
METHOD
Steps for VLSM
List every segment with the number of hosts it needs, largest first
Subnet the block to fit the largest segment, and assign it the first subnet
Take the next free subnet and split it again for the second-largest segment
Repeat, each time subdividing free space rather than touching what is already assigned
Finish with the point-to-point links, which need only two addresses each
Always work largest to smallest. Start with the small segments and the big one will no longer fit anywhere.
VLSM
22

## Slide 23
CASE STUDY
The Requirement
Three Departments
Development: 74 hosts
Production: 52 hosts
Administrative: 28 hosts
Three WAN Links
Each link joins two routers
Each needs 2 usable addresses
Six subnets in total, about 160 host addresses
The Block
One private /24: 192.168.1.0/24
254 usable addresses in total
Enough — but only if each subnet is sized properly
VLSM Case Study
23

## Slide 24
CASE STUDY
The Allocation
Development — /25
192.168.1.0/25
Mask 255.255.255.128
126 usable, 74 needed
Range .1 to .126, broadcast .127
Production — /26
192.168.1.128/26
Mask 255.255.255.192
62 usable, 52 needed
Range .129 to .190, broadcast .191
Administrative — /27
192.168.1.192/27
Mask 255.255.255.224
30 usable, 28 needed
Range .193 to .222, broadcast .223
WAN Links — /30
192.168.1.224/30
192.168.1.228/30
192.168.1.232/30
Mask 255.255.255.252, 2 usable each
VLSM Case Study
24

## Slide 25
CASE STUDY
The Result
All six segments are addressed from a single /24 — no second block had to be bought
Development took .0 to .127, production .128 to .191, administrative .192 to .223
The three WAN links took .224 to .235, twelve addresses in total
That leaves 192.168.1.236 to .255 — twenty addresses still free for growth
With one fixed mask the same network would not have fitted in a /24 at all
Modern practice: a point-to-point link can use a /31 (RFC 3021), giving two usable addresses with no network ID or broadcast wasted. Check your platform supports it before relying on it.
VLSM Case Study
25

## Slide 26
CHECK YOUR UNDERSTANDING
Checkpoint 2 — Subnetting and VLSM
QUESTION 4
How many usable host addresses does a /27 provide?
A. 32
B. 30
C. 28
D. 62
QUESTION 5
Which prefix is normally used for a point-to-point WAN link?
A. /28
B. /29
C. /30
D. /24
QUESTION 6
In VLSM, in what order do you allocate the segments?
A. Smallest first
B. Largest first
C. WAN links first
D. Any order works
Checkpoint
26

## Slide 27
WHERE WE STAND
IPv4 Is Full — IPv6 Is the Answer
IANA handed out its last free IPv4 blocks in February 2011; the regional registries followed, AFRINIC among them
IPv4 addresses are now bought and leased on an open market, which is why every address on your bill costs money
IPv6 uses 128 bits instead of 32, so the address space is effectively unlimited
On 28 March 2026 IPv6 passed half of all traffic to Google for the first time, at 50.1%
APNIC’s independent measure is lower, around 42%, and African adoption still trails badly — a gap worth closing
Sources: Google IPv6 statistics and APNIC Labs, April 2026. NAT and CIDR bought IPv4 thirty extra years; they did not make it infinite.
IPv4 and IPv6
27

## Slide 28
ASSESSMENT
How You'll Be Assessed
Each lab step is verified before the group moves on — the instructor checks your addressing against the plan
You will be asked to justify a subnet, not just write one: why this mask, why this size
A wrong address shows up as a failed ping, so diagnosis counts for as much as configuration
Checkpoint questions between sections are formative, not graded
Success criteria — by the close of this session each group can size a subnet from a host count, write the network ID, first host, last host and broadcast for it, and explain why the WAN link is a /30.
Assessment
28

## Slide 29
SUMMARY
Key Takeaways
An IPv4 address is 32 bits; the mask decides where the network part stops and the host part starts
Learn 128 64 32 16 8 4 2 1 and you can subnet on paper, without a calculator
Usable hosts are always two fewer than the block size — the network ID and the broadcast are not hosts
Classes are history; CIDR lets the prefix fall wherever the network actually needs it
VLSM sizes every subnet to its segment, largest first — that is how one /24 serves six networks
Summary
29

## Slide 30
INSTRUCTOR NOTES
Answer Key
Question 1 B
301 exceeds 255. An octet is 8 bits, so no octet can be higher than 255.
Question 2 B
The prefix counts network bits. /26 means 26 network bits, leaving 6 for hosts.
Question 3 B
RFC 1918 reserves 172.16.0.0/12, which covers 172.16 to 172.31. 172.168 is public space.
Question 4 B
A /27 leaves 5 host bits: 2⁵ = 32 addresses, minus the network ID and broadcast = 30.
Question 5 C
A /30 gives exactly 2 usable addresses, one for each router. A /31 is the modern alternative.
Question 6 B
Allocate largest first. Starting small fragments the block and the big segment no longer fits.
Answer Key — remove for student handout
30

## Slide 31
Questions?
IP Addressing & Subnetting — Network Infrastructure Workshop, SomNOG9
Based on original materials by the Network Startup Resource Center (NSRC, nsrc.org)
Licensed under Creative Commons Attribution-NonCommercial 4.0 International