## Slide 1
NETWORK INFRASTRUCTURE WORKSHOP · SOMNOG9
Cisco Configuration Introduction
Modes, Commands, Verification and Poor Defaults
Track 1 — Network Infrastructure · SNU KM4 Campus, Mogadishu

## Slide 2
LEARNING OBJECTIVES
By the End of This Session
Tell the running configuration from the startup configuration, and say what happens to each on reboot
Move between user, privileged and configuration mode, and read the prompt to know where you are
Use context help, tab completion and command shorthand to work faster and make fewer mistakes
Verify a device with the show commands, and undo a command by negating it
Fix the two legacy defaults that make every fresh Cisco device unpleasant to work on
Learning Objectives
2

## Slide 3
AGENDA
What We'll Cover
Cisco devices and IOS, and where the configuration actually lives
How you get in: console, auxiliary port, and virtual terminals
Access modes, the command structure, and saving your work
Help, completion, shorthand and line editing
Verifying, troubleshooting, undoing, and fixing poor defaults
Agenda
3

## Slide 4
IN TODAY’S LAB
From Concept to Console
Lab 1 is basic housekeeping — this session is the reference you will keep open while you do it
You start on the console cable, because a switch with no address cannot be reached any other way
Everything you type takes effect immediately. There is no apply button and no undo button
Save with write memory as you go — the device will not do it for you, and power cuts do happen
Fix the poor defaults at the end of this session before you start the VLAN labs, or logging will fight you all day
Every later lab assumes you can get onto a device, see where you are from the prompt, and save your work. That is all Lab 1 is.
In Today's Lab
4

## Slide 5
BACKGROUND
Introduction to Cisco Devices
This session covers Cisco routers and switches running Cisco IOS
IOS is the Internetwork Operating System — the software that controls the router or switch
IOS-XE has replaced classic IOS on most current platforms
IOS-XR runs on high-end service provider routers; NX-OS runs on Nexus data centre switches
Equipment from other vendors uses the same concepts with different words
Background
5

## Slide 6
CONFIGURATION
Where Is the Configuration?
running-config
Stored in RAM
The parameters currently in use
Changed with configure terminal
View it with show running-config
Lost completely if the device reboots before you save
startup-config
Stored in NVRAM
Loaded by the device at the next boot
This is where the running config is saved to
View it with show startup-config
Survives a reboot and a power cut
Every device has both. The gap between them is where most lost work lives.
Configuration
6

## Slide 7
ACCESS
Management Input Sources
Console
Direct access over the serial port
Works with no IP address configured
The only way in on a brand new device
This is where Lab 1 starts
Auxiliary Port
Access by modem or another serial device
Also used to reach other serial devices from the router
Rare on modern equipment
Virtual Terminals (VTY)
Telnet or SSH across the network
Needs an IP address and a working path first
Use SSH — Telnet sends your password in clear text
Access
7

## Slide 8
ACCESS
Getting Connected, and Being Careful
Any terminal emulator will do: PuTTY, Tera Term, SecureCRT, screen, or the macOS and Linux terminal
Commands take effect the moment you press enter — there is no apply step
You can paste a prepared block of configuration into the terminal, but check it line by line first
A mistyped paste on a live device is one of the most common ways to lose remote access
Configuration can also be copied in from a TFTP or SCP server
Access
8

## Slide 9
MODES
Access Modes
Router> user mode: limited status only
Router> enable
Router# privileged mode: full view
Router# configure terminal
Router(config)# configuration mode
Router(config)# end (or Ctrl-Z) back to privileged
Router# disable back to user mode
Router> exit log off
The prompt always tells you where you are — read it before you type
A > means user mode, a # means privileged, and (config) means you are changing things
Sub-modes appear as you go deeper, for example Router(config-if)# for an interface
Modes
9

## Slide 10
SYNTAX
The IOS Command Structure
A command starts with a keyword that says what to do: show, configure, interface, ip
Keywords are followed by arguments — the values you supply, such as an address or a name
Commands are entered in the mode that owns them; an interface command needs interface mode first
Almost every configuration command can be reversed by putting no in front of it
Nothing is case sensitive, and nothing needs to be typed in full — see the next few slides
Syntax
10

## Slide 11
SAVING
Saving the Configuration
Router# write memory
Router# wr the same thing, shortened
Router# copy running-config startup-config the long form
Router# copy running-config ?
flash: Copy to flash: file system
ftp: Copy to ftp: file system
scp: Copy to scp: file system
startup-config Copy to startup configuration
tftp: Copy to tftp: file system
The device does not save automatically. If you reboot without saving, your work is gone
Saving is done from privileged mode
The configuration can also be copied off the device to a TFTP or SCP server as a backup
Saving
11

## Slide 12
CHECK YOUR UNDERSTANDING
Checkpoint 1 — Modes and Saving
QUESTION 1
Which configuration is lost when the device reboots?
A. startup-config
B. running-config
C. Both of them
D. Neither of them
QUESTION 2
You have just made changes. Which command keeps them across a reboot?
A. show running-config
B. copy running-config startup-config
C. reload
D. configure terminal
QUESTION 3
You are at the Router> prompt. How do you reach privileged mode?
A. configure terminal
B. enable
C. end
D. disable
Checkpoint
12

## Slide 13
HELP
Context and Online Help
Router(config)# ? list every command available here
aaa Authentication, Authorization and Accounting
access-list Add an access list entry
alias Create command alias
arp Set a static ARP entry
Router(config)# username ? what comes next?
WORD User name
Router(config)# username cndlab ?
password Specify the password for the user
A question mark on its own lists the commands valid in your current mode
A question mark after a partial command shows the parameters it will accept
This works at every level, so you can build a long command one step at a time
Help
13

## Slide 14
EFFICIENCY
Completion and Shorthand
Router(config)# int<TAB>
Router(config)# interface fa<TAB>
Router(config)# interface fastEthernet 0
Router(config-if)# ip add<TAB>
Router(config-if)# ip address n.n.n.n m.m.m.m
Router(config)# int fa 0 shorthand works without TAB too
Router(config-if)# ip add 192.168.1.1 255.255.255.0
Router(config-if)# no sh
Router# sh ip int br
Tab completes a command as long as what you have typed so far is unambiguous
IOS also accepts the shortened form directly, which is what you will see in most documentation
Write commands out in full in your notes and your change plans — shorthand is for typing, not for recording
Efficiency
14

## Slide 15
EFFICIENCY
Moving Around the Command Line
Up arrow / Ctrl-P
Previous command in the history
Down arrow / Ctrl-N
Next command in the history
Left arrow / Ctrl-B
Move one character left
Right arrow / Ctrl-F
Move one character right
Ctrl-A
Jump to the beginning of the line
Ctrl-E
Jump to the end of the line
Ctrl-K
Delete from the cursor to the end of the line
Ctrl-W
Delete the word before the cursor
Ctrl-Z
Leave configuration mode entirely
These are the same key bindings as a Unix shell. Learning them once pays off on every device you ever touch.
Efficiency
15

## Slide 16
VERIFYING
Checking the Configuration
Router# show running-config what is in use right now
Router# show startup-config what will load at next boot
Router# show configuration an alias for show startup-config
Router# show running-config interface Gig0/0
just one interface
These need privileged mode
Comparing running against startup tells you whether anything is unsaved
Narrowing to one interface saves you scrolling through hundreds of lines
Verifying
16

## Slide 17
VERIFYING
Checking Interfaces
Router# show interface Gig0/0 one interface in full detail
Router# show interfaces description all of them, one line each
Interface Status Protocol Description
Fa0/0 up up Backbone LAN
Fa0/1 up up Server LAN
Lo0 up up Loopback
Router# show ip interface brief IPv4 status of every interface
Router# show ipv6 interface brief the same for IPv6
Status is the physical layer; protocol is the data link layer. Both must be up
up / down means the cable is fine but the line protocol is not — look at encapsulation or keepalives
show ip interface brief is the single most used command on a Cisco device
Verifying
17

## Slide 18
VERIFYING
Neighbours, Logs and Version
Router# show cdp neighbors directly attached Cisco devices
Router# show lldp neighbors the vendor-neutral equivalent
Router# show logging the log buffer
Router# show version software and hardware detail
CDP is Cisco-only. LLDP is the IEEE standard and works across vendors
Both tell you what is plugged into what, which beats tracing a cable by hand
show version gives the IOS image, uptime, serial number and installed memory
Verifying
18

## Slide 19
EFFICIENCY
The do Command
Router(config)# do show interface Gig0/0
Router(config)# do show ip interface brief
Router(config)# do write memory
do lets you run a privileged mode command without leaving configuration mode
Much quicker than exiting, checking, and going back in
Particularly useful for checking your own change before you move on to the next one
Efficiency
19

## Slide 20
UNDOING
Undoing Configuration
Router# show run interface fa0/0
interface FastEthernet0/0
description Link to Core-Router
ip address 192.168.1.10 255.255.255.224
Router# configure terminal
Router(config)# interface fa0/0
Router(config-if)# no ip address
Router(config-if)# end
Router# show run interface fa0/0
interface FastEthernet0/0
description Link to Core-Router
To undo a command, negate it — put no in front of the command you originally typed
The address is gone; the description was never negated, so it stays
This works for almost every configuration command in IOS
Undoing
20

## Slide 21
CHECK YOUR UNDERSTANDING
Checkpoint 2 — Verifying and Undoing
QUESTION 4
How do you remove an IP address you configured on an interface?
A. delete ip address
B. no ip address
C. clear ip address
D. erase ip address
QUESTION 5
Which keyword runs a privileged command without leaving configuration mode?
A. exit
B. do
C. end
D. run
QUESTION 6
Log messages keep interrupting what you are typing on the console. What fixes it?
A. no logging console, and log to the buffer instead
B. no ip domain-lookup
C. logging console debugging
D. write memory
Checkpoint
21

## Slide 22
POOR DEFAULTS
Log Messages Interrupt Your Typing
Router(config-if)# ip addre*Jun 20 07:53:55.755: %LINEPROTO-5-UPDOWN:
Line protocol on Interface GigabitEthernet3/0, changed state to downss 1.2.3.4
Router(config)# no logging console
Router(config)# logging buffered 8192 debugging
Router# show logging read the buffer instead
By default log messages are printed straight to the console, mixed into whatever you are typing
The line above is a real address command destroyed by a log message arriving mid-word
Turn console logging off and log to memory, then read it when you want to
Poor Defaults
22

## Slide 23
POOR DEFAULTS
DNS Lookups Go to a Broadcast
Router# ping somnog.org
Translating “somnog.org"...domain server (255.255.255.255)
% Unrecognized host or address, or protocol not running.
Router(config)# no ip domain-lookup turn it off entirely
Router(config)# ip name-server 8.8.8.8 or configure real servers
Router(config)# ip name-server 8.8.4.4
By default a mistyped command is treated as a hostname and sent to a broadcast address
The device then sits there for many seconds while you wait for it to give up
Disabling lookups is the usual choice in a lab; real name servers are the choice in production
Even with real servers, a lookup will still hang if the network is down
Poor Defaults
23

## Slide 24
ASSESSMENT
How You'll Be Assessed
Each lab step is verified before the group moves on — the instructor checks your device, not your screenshot
You are assessed on getting onto the device, knowing which mode you are in, and saving your work
You will be asked to undo something you configured, and to show that it is gone
Checkpoint questions between sections are formative, not graded
Success criteria — by the close of Lab 1 each group can reach both switches by console, move between the three modes, save the configuration, and has fixed both poor defaults.
Assessment
24

## Slide 25
SUMMARY
Key Takeaways
running-config is in RAM and disappears on reboot; startup-config is in NVRAM and survives
The prompt tells you which mode you are in — read it before you type anything
The question mark, tab completion and shorthand are how experienced operators work quickly
Undo by negating: no in front of the command you typed
Fix console logging and DNS lookups on every new device before you do anything else
Summary
25

## Slide 26
INSTRUCTOR NOTES
Answer Key
Question 1 B
running-config lives in RAM. Without a save it is gone at the next reboot.
Question 2 B
copy running-config startup-config, or its short forms write memory and wr.
Question 3 B
enable moves from user mode to privileged mode, and the prompt changes from > to #.
Question 4 B
Negate the original command: no ip address.
Question 5 B
do runs a privileged command from inside configuration mode.
Question 6 A
no logging console stops the interruptions; logging buffered keeps the messages readable.
Answer Key — remove for student handout
26

## Slide 27
Questions?
Cisco Configuration Introduction — Network Infrastructure Workshop, SomNOG9
Based on original materials by the Network Startup Resource Center (NSRC, nsrc.org)
Licensed under Creative Commons Attribution-NonCommercial 4.0 International