## Slide 1
NETWORK INFRASTRUCTURE WORKSHOP · SOMNOG9
Network Address Translation
Static NAT, Dynamic NAT and Overload on Cisco IOS
Track 1 — Network Infrastructure · SNU KM4 Campus, Mogadishu

## Slide 2
LEARNING OBJECTIVES
By the End of This Session
Explain why NAT exists, and why it is a stopgap rather than a solution
Use the four NAT address terms correctly — inside local, inside global, outside local, outside global
Tell static NAT, dynamic NAT and PAT apart, and choose the right one for a given requirement
Read and write a working NAT configuration on Cisco IOS, including the ACL that selects the traffic
Verify a translation with show ip nat translations, and explain what NAT breaks
Learning Objectives
2

## Slide 3
AGENDA
What We'll Cover
Why NAT exists — IPv4 exhaustion and the short-term fix
The four addressing terms, and how to read them off a packet
Static NAT, dynamic NAT, and overload (PAT)
A campus use case, and the Cisco configuration that implements it
Verification, and the things NAT quietly breaks
Agenda
3

## Slide 4
IN TODAY’S LAB
From Concept to Console
Lab 13 is the last step, and it is instructor-led on the core router
It happens only once every group’s routes have been received — NAT is pointless if the routing is not finished
Your pod keeps its private addressing; the core router translates it on the way out
You will watch the translation table build as your own traffic leaves, and find your own entry in it
Everything you configured in Labs 1–12 has to be working before this slide becomes useful
NAT hides a routing problem rather than fixing it. If your peer group is unreachable, that is a Lab 11 or 12 issue — do not expect NAT to paper over it.
In Today's Lab
4

## Slide 5
MOTIVATION
Why NAT Exists
IPv4 has only about 4.3 billion addresses, and they were allocated far faster than anyone planned for
IANA handed out its last free IPv4 blocks in February 2011, and the regional registries followed
CIDR and VLSM slowed the burn rate but could not create new address space
NAT was the short-term answer: let many private hosts share a handful of public addresses
IPv6 is the long-term answer, with a 128-bit address space — it passed half of Google’s traffic in March 2026
NAT has kept IPv4 alive for over twenty-five years. That is an achievement and a problem at the same time — it removed the urgency to deploy IPv6.
Motivation
5

## Slide 6
CONCEPT
What NAT Actually Does
The Private Side
Uses RFC 1918 space — 10.0.0.0/8, 172.16.0.0/12, 192.168.0.0/16
These addresses are not unique and are never routed on the Internet
Every organisation may use the same ranges
The Public Side
Uses globally unique addresses assigned through a registry
Routable across the Internet
Scarce and expensive, which is the whole reason NAT exists
The Router in Between
Rewrites the source address as a packet leaves
Remembers the mapping in a translation table
Reverses the rewrite on the reply so it reaches the right host
Concept
6

## Slide 7
TERMINOLOGY
The Four NAT Address Terms
Inside Local
The real private address of a host inside your network
What the host itself believes its address is
For example 192.168.1.10
Inside Global
The public address that same inside host appears as from outside
What a server on the Internet sees as the source
For example 100.64.10.2
Outside Global
The real public address of a host out on the Internet
The address you were actually trying to reach
For example 8.8.8.8
Outside Local
How that outside host appears to your inside network
Usually identical to outside global
Differs only where the outside address is also translated
Inside and outside say where the host lives. Local and global say which side of the router you are standing on when you read the address.
Terminology
7

## Slide 8
WORKED EXAMPLE
Naming the Addresses
QUESTION
A PC on 192.168.1.10 browses a server at 8.8.8.8. The border router translates it to 100.64.10.2. Name each address.
192.168.1.10 → 100.64.10.2 → 8.8.8.8
SOLUTION
192.168.1.10 is the inside local. 100.64.10.2 is the inside global.
8.8.8.8 is both the outside global and, because it is not translated, the outside local as well.
Terminology
8

## Slide 9
TYPES
Three Kinds of NAT
Static NAT
One private address permanently mapped to one public address
The mapping exists whether or not there is traffic
Use it when a device must be reachable from outside — a web or mail server
192.168.32.10 always becomes 213.18.123.110
Dynamic NAT
Private addresses mapped to a pool of public addresses, first come first served
The mapping lasts only as long as the session
Runs out when more hosts want out than the pool has addresses
Rarely used on its own today
PAT / Overload
Many private addresses share one public address, separated by port number
Also called NAPT or port address translation
This is what almost every network actually runs
One public address can serve thousands of hosts
Types of NAT
9

## Slide 10
TYPES
How Overload Works
The router rewrites both the source address and the source port on the way out
Each conversation gets a unique port on the public address, so replies can be matched back
The translation table holds the tuple: inside address and port, public address and port, destination
A single public address has roughly 64,000 usable ports, so thousands of hosts fit behind it
Entries are removed when the session closes or the idle timer expires
Types of NAT
10

## Slide 11
CHECK YOUR UNDERSTANDING
Checkpoint 1 — Concepts and Types
QUESTION 1
A host is 192.168.1.10 inside and appears outside as 100.64.10.2. What is 192.168.1.10 called?
A. Inside global
B. Inside local
C. Outside local
D. Outside global
QUESTION 2
Which form of NAT lets many private hosts share one public address?
A. Static NAT
B. Dynamic NAT
C. PAT, also called overload
D. None — that is impossible
QUESTION 3
A web server inside must be reachable from the Internet. Which NAT do you use?
A. Static NAT
B. Dynamic NAT
C. Overload
D. No NAT is possible
Checkpoint
11

## Slide 12
USE CASE
A Campus That Runs Out of Addresses
The upstream provider gives the campus a single /28 — sixteen addresses for the whole institution
That /28 is split into two /29s: one for services that genuinely need public addresses, one for translation
Public-facing servers sit in the first /29 and are reached directly, no NAT involved
Everything else — every office, lab and classroom — uses RFC 1918 space internally
The border router translates all of that private space onto the second /29 on the way out
The example addresses use 100.64.0.0/10. That block is RFC 6598 shared space, reserved for carrier-grade NAT — it stands in for public addressing in teaching material, but never use it as your own public range.
Use Case
12

## Slide 13
CONFIGURATION
Step 1 — Select the Traffic
ip access-list extended NATplus
deny ip 100.64.10.0 0.0.0.255 any
deny ip 192.168.0.0 0.0.255.255 192.168.0.0 0.0.255.255
permit ip 192.168.0.0 0.0.255.255 any
deny ip any any log
The ACL does not filter traffic here — it selects which traffic gets translated
Do not translate your own public range, and do not translate internal-to-internal traffic
Translate internal sources heading anywhere outside
The final deny with log catches anything unexpected, which is how you find mistakes
Configuration
13

## Slide 14
CONFIGURATION
Step 2 — Mark Inside and Outside
interface GigabitEthernet0/1
description Link to ISP
ip address 100.64.10.2 255.255.255.252
ip nat outside
!
interface GigabitEthernet0/2
description Link to Campus Core Switch
ip address 192.168.255.1 255.255.255.252
ip nat inside
Every NAT configuration needs exactly one inside and one outside direction
Outside faces the provider; inside faces the campus
Getting these the wrong way round is the most common reason NAT silently does nothing
Configuration
14

## Slide 15
CONFIGURATION
Step 3 — Translation Timeouts
ip nat translation dns-timeout 60
ip nat translation icmp-timeout 180
ip nat translation udp-timeout 300
ip nat translation finrst-timeout 60
ip nat translation tcp-timeout 3600
A timeout is how long an idle mapping is kept before the router reclaims it
The first four are Cisco defaults; the TCP value is lowered from 86,400 seconds to 3,600
Long timeouts waste table space; short ones break long-lived idle sessions such as SSH
Configuration
15

## Slide 16
CONFIGURATION
Step 4a — Overload Onto One Address
ip nat inside source list NATplus interface GigabitEthernet0/1 overload
Traffic matching NATplus, moving from inside to outside, is translated
overload means PAT — one address shared by many hosts, separated by port
The address used is whatever is configured on GigabitEthernet0/1
The whole campus then appears on the Internet as 100.64.10.2
Configuration
16

## Slide 17
CONFIGURATION
Step 4b — Overload Onto a Pool
ip nat pool CAMPUS 100.64.10.65 100.64.10.70 prefix-length 29
ip nat inside source list NATplus pool CAMPUS overload
A pool spreads the load across several public addresses instead of one
The pool here takes the usable addresses of the second /29, leaving out the network and broadcast addresses
overload still applies, so each pool address can itself serve many hosts
Use a pool when one address cannot hold enough simultaneous translations
Configuration
17

## Slide 18
VERIFICATION
Checking That It Works
show ip nat translations
show ip nat statistics
clear ip nat translation *
debug ip nat
show ip nat translations lists every active mapping — find your own host in it
show ip nat statistics gives hit and miss counts, and confirms which ACL and interfaces are in use
clear ip nat translation * wipes the table, which is useful after changing the configuration
debug ip nat prints every translation as it happens — informative in a lab, dangerous in production
Verification
18

## Slide 19
LIMITS
What NAT Breaks
End-to-end addressing is gone — a host no longer knows the address the world sees it as
Inbound connections do not work by default, because no translation exists until an inside host starts a session
Protocols that carry addresses inside the payload need help, which is why routers ship application-layer gateways
Troubleshooting is harder: logs on the far side show one address for thousands of users
Carrier-grade NAT stacks a second layer of this on top, and makes it worse again
None of these are reasons to avoid NAT — you have no choice on IPv4. They are reasons to deploy IPv6 alongside it.
Limits
19

## Slide 20
CHECK YOUR UNDERSTANDING
Checkpoint 2 — Configuration and Limits
QUESTION 4
Which command shows the router’s current translation table?
A. show ip nat statistics
B. show ip nat translations
C. show ip route
D. show access-lists
QUESTION 5
Which interface is configured with ip nat outside?
A. The one facing the campus
B. The one facing the ISP
C. Both interfaces
D. Neither — it goes on the pool
QUESTION 6
Why do inbound connections fail through a NAT router by default?
A. NAT encrypts the payload
B. No translation entry exists until an inside host starts a session
C. NAT drops all TCP traffic
D. The IP header is removed
Checkpoint
20

## Slide 21
ASSESSMENT
How You'll Be Assessed
This lab is instructor-led on the core router — you follow the configuration as it is built
You are assessed on finding your own pod’s traffic in the translation table and explaining the entry
You will be asked which address is inside local and which is inside global for your own host
Checkpoint questions between sections are formative, not graded
Success criteria — by the close of this session each group can point at its own entry in show ip nat translations, name all four addresses in it, and say what would happen if the inside and outside interfaces were swapped.
Assessment
21

## Slide 22
SUMMARY
Key Takeaways
NAT exists because IPv4 ran out — it buys time, it does not create address space
Inside and outside say where a host lives; local and global say which side you are reading from
Static NAT for servers, dynamic NAT rarely, overload for everything else
The ACL selects traffic, the interfaces set direction, and one line activates the translation
NAT breaks inbound connections and end-to-end addressing — which is the argument for IPv6
Summary
22

## Slide 23
INSTRUCTOR NOTES
Answer Key
Question 1 B
Inside local: the real private address of a host inside your network.
Question 2 C
PAT, or overload, separates conversations by port so many hosts share one address.
Question 3 A
Static NAT keeps a permanent mapping, so the server is reachable without inside traffic first.
Question 4 B
show ip nat translations lists the active mappings. Statistics gives counters, not entries.
Question 5 B
Outside faces the provider. Inside faces the campus. Swapping them stops NAT working.
Question 6 B
The table is built by outbound traffic, so there is nothing to reverse an inbound packet onto.
Answer Key — remove for student handout
23

## Slide 24
Questions?
Network Address Translation — Network Infrastructure Workshop, SomNOG9
Based on original materials by the Network Startup Resource Center (NSRC, nsrc.org)
Licensed under Creative Commons Attribution-NonCommercial 4.0 International