## Slide 1
NETWORK INFRASTRUCTURE WORKSHOP · SOMNOG9
Introduction to Routing
Static Routes, Default Routes and Routing Protocols
Track 1 — Network Infrastructure · SNU KM4 Campus, Mogadishu

## Slide 2
LEARNING OBJECTIVES
By the End of This Session
Explain what a router does with a packet whose destination is outside the local network
State the order a router uses to pick a route — longest prefix first, then administrative distance, then metric
Write a static route and a default route on Cisco IOS, and read one back from the running config
Tell a routed protocol from a routing protocol, and an IGP from an EGP
Compare distance-vector and link-state behaviour, and say why OSPF is trusted over RIP
Learning Objectives
2

## Slide 3
AGENDA
What We'll Cover
What routing is, and how a router chooses between competing routes
Static routes, default routes, and when a floating static earns its place
Dynamic routing — what a routing protocol actually does for you
Classifying protocols: IGP and EGP, distance-vector, link-state and path-vector
Metrics, administrative distance, convergence, and autonomous systems
Agenda
3

## Slide 4
IN TODAY’S LAB
From Concept to Console
Lab 10: bring up your router — Fa0/0 as a routed port into your own SW1, Fa0/1 to the next group
Lab 11: write static routes to reach your peer group’s networks across that direct cable
Lab 12: delete every static route and restore the same reachability with OSPF
Lab 13: NAT on the core router, instructor-led, once all group routes have been received
Static first is deliberate — you will feel the maintenance cost before OSPF removes it
Your peer group gives you the address on your Fa0/1 link. Agree the subnet with them before either of you configures anything.
In Today's Lab
4

## Slide 5
FUNDAMENTALS
What Routing Is
Routing is deciding where to send a packet whose destination is outside the local network
A switch forwards within one network; a router forwards between networks
Every router keeps a routing table — a list of destination prefixes and how to reach each one
For every packet the router asks one question: which entry in my table matches this destination?
If nothing matches and there is no default route, the packet is dropped and the sender is told
Fundamentals
5

## Slide 6
DECISION ORDER
How a Router Picks a Route
First, longest prefix match. A /24 entry beats a /16 entry for the same destination, whatever learned it
Only if two routes have the same prefix length does administrative distance decide — lower is more trusted
Only if prefix and distance both tie does the protocol metric decide — lower cost wins
If everything ties, the router installs several paths and load-balances across them
Getting this order the wrong way round is the single most common routing misconception
Longest prefix always comes first. A static /16 does not beat an OSPF /24, even though static has the lower distance.
Fundamentals
6

## Slide 7
ROUTE TYPES
Three Ways a Route Gets Into the Table
Connected
Appears automatically when an interface has an address and is up
Administrative distance 0 — the most trusted route there is
Disappears the moment the interface goes down
Static
You type it in by hand
Administrative distance 1
Good for small, stable networks and for a default route
Every change is manual work, and it does not react to a failure
Dynamic
Learned from a neighbour running the same routing protocol
Distance depends on the protocol — OSPF 110, RIP 120
Adapts automatically when the topology changes
Route Types
7

## Slide 8
STATIC ROUTING
Static Routes
Use a static route when the path is fixed, the network is small, or you want no protocol overhead
Configured in global configuration mode, one line per destination network
You give it the destination network, the mask, and either a next-hop address or an exit interface
Next-hop is usually safer than exit interface on a multi-access link such as Ethernet
The optional distance at the end is what turns an ordinary static into a floating static
ip route <destination-network> <subnet-mask> {<next-hop-address> | <exit-interface>} [distance]
Static Routing
8

## Slide 9
WORKED EXAMPLE
Writing a Static Route
QUESTION
Your peer group owns 10.5.0.0/16. You reach them through the router at 172.16.1.2 on your Fa0/1. Write the route.
R1(config)# ?
SOLUTION
ip route 10.5.0.0 255.255.0.0 172.16.1.2
Destination network, then mask in dotted decimal, then the next hop. Check it afterwards with show ip route static.
Static Routing
9

## Slide 10
STATIC ROUTING
Default Routes
A default route is a static route that matches every destination — 0.0.0.0 with mask 0.0.0.0, written 0.0.0.0/0
It is used only when no more specific entry matches, because longest prefix match comes first
Also called the gateway of last resort
The usual case is an edge router pointing at the ISP: everything not local goes that way
On Cisco IOS: ip route 0.0.0.0 0.0.0.0 <next-hop>
Static Routing
10

## Slide 11
STATIC ROUTING
Floating Static Routes
A floating static is an ordinary static route given a deliberately high administrative distance
Because its distance is worse than the dynamic protocol’s, it stays out of the routing table
If the dynamic route disappears, the floating static is installed and traffic keeps flowing
Typical use: a backup link that should carry traffic only when the primary path fails
Example: ip route 0.0.0.0 0.0.0.0 192.0.2.1 200 — distance 200 sits behind OSPF at 110
Static Routing
11

## Slide 12
CHECK YOUR UNDERSTANDING
Checkpoint 1 — Static and Default Routing
QUESTION 1
A router knows 10.0.0.0/8 via OSPF and 10.5.0.0/16 via RIP. A packet for 10.5.1.1 arrives. Which is used?
A. The OSPF route — lower administrative distance
B. The RIP route — longer prefix match
C. Neither — the packet is dropped
D. Both — traffic is load-balanced
QUESTION 2
What is the administrative distance of a static route on Cisco IOS?
A. 0
B. 1
C. 110
D. 120
QUESTION 3
Which entry is a default route?
A. 0.0.0.0 0.0.0.0
B. 255.255.255.255
C. 127.0.0.1 255.0.0.0
D. 224.0.0.0 240.0.0.0
Checkpoint
12

## Slide 13
DYNAMIC ROUTING
What a Routing Protocol Does
Discovers remote networks by talking to neighbouring routers running the same protocol
Keeps that information current as links come up and go down
Chooses the best path to each destination using its own metric
Finds a new best path automatically when the current one fails
The trade is overhead: CPU, memory and control traffic in exchange for not maintaining routes by hand
Dynamic Routing
13

## Slide 14
TERMINOLOGY
Routed Protocol or Routing Protocol?
Routed Protocol
The protocol the data itself is carried in
Its address is complete enough for a router to forward the packet one hop further
No router needs to know the whole path — only the next hop
IP is the example that matters
Routing Protocol
The protocol routers use to talk to each other about paths
Builds and maintains the routing table automatically
Carries no user data of its own
RIP, OSPF, EIGRP and BGP are examples
One carries your traffic, the other tells routers where to send it. IP is routed; OSPF is a routing protocol.
Dynamic Routing
14

## Slide 15
CLASSIFICATION
IGP and EGP
Interior Gateway Protocols
Used inside one autonomous system
RIPv2, EIGRP, OSPF and IS-IS
Optimised for fast convergence within your own network
OSPF is what you configure in Lab 12
Exterior Gateway Protocols
Used between autonomous systems
BGP is the only one in real use today
Optimised for policy and scale rather than speed
This is how networks exchange routes across the Internet
Classification
15

## Slide 16
CLASSIFICATION
Three Families of Routing Protocol
Distance Vector
Advertises routes as a distance and a direction
Each router trusts what its neighbour tells it
No full view of the topology
Updates are generally periodic
RIP is the classic example
Link State
Every router floods the state of its own links
Each builds a complete map and runs SPF on it
Updates are event-driven, not periodic
Converges quickly and predictably
OSPF and IS-IS
Path Vector
Carries the full list of autonomous systems a route has crossed
Uses that path to detect and reject loops
Chooses on policy rather than on a speed metric
BGP
Classification
16

## Slide 17
CLASSIFICATION
Classful and Classless
Classful
Does not send the subnet mask in its updates
The receiver has to assume a mask from the address class
Cannot support VLSM or discontiguous networks
RIPv1 and IGRP — both obsolete
Classless
Sends the prefix length with every route
Supports VLSM, CIDR and route summarisation
Everything you would deploy today
RIPv2, EIGRP, OSPF, IS-IS and BGP
This is the same story as the addressing session: classes stopped deciding anything once CIDR arrived in 1993.
Classification
17

## Slide 18
BEHAVIOUR
Convergence
A network has converged when every router’s routing table agrees about the topology
Until then some routers still believe in a path that no longer exists
During that window traffic can loop, or be dropped, or take a longer path than it should
Link-state protocols converge faster because a change is flooded immediately, not waited out
Convergence time is the honest measure of a routing design — it is what your users actually feel
Behaviour
18

## Slide 19
BEHAVIOUR
Metrics
A metric is the number a routing protocol uses to decide which of several paths is better
Hop count — how many routers the packet passes through. Simple, and blind to link speed. RIP uses this
Bandwidth — the capacity of a link. A 1 Gbps path beats a 64 kbps one even if it is longer
Delay, load and reliability — additional characteristics some protocols combine into one value
Cost — on Cisco routers, derived from interface bandwidth by default. This is what OSPF uses
Behaviour
19

## Slide 20
TRUST
Administrative Distance
0
Connected interface — the router can see it directly
1
Static route — you configured it, so it is trusted next
20
External BGP
90
Internal EIGRP, within the same autonomous system
110
OSPF
115
IS-IS
120
RIPv1 and RIPv2
170
External EIGRP, redistributed from another AS
200
Internal BGP
255
Unusable — the route will never be installed
Administrative distance only breaks a tie between routes with the same prefix length. It is a measure of trust, not of quality.
Trust
20

## Slide 21
SCOPE
Autonomous Systems
An autonomous system is a group of networks under one administrative control
That might be a company, a division, or an ISP
AS numbers are globally assigned, and BGP uses them to describe the path a route has taken
EIGRP, OSPF, IS-IS and BGP all understand the concept; RIP does not
OSPF has an area and a process ID but does not ask you for an AS number; EIGRP does
Scope
21

## Slide 22
CHECK YOUR UNDERSTANDING
Checkpoint 2 — Dynamic Routing
QUESTION 4
Which of these is an exterior gateway protocol?
A. OSPF
B. EIGRP
C. BGP
D. RIPv2
QUESTION 5
Which statement describes a link-state protocol?
A. It advertises routes as a distance and a direction
B. Each router builds a complete map of the topology
C. It sends its whole routing table periodically
D. It ignores link bandwidth entirely
QUESTION 6
The same /24 is learned by OSPF and by a static route. Which is installed?
A. The OSPF route
B. The static route
C. Both, load-balanced
D. Neither
Checkpoint
22

## Slide 23
ASSESSMENT
How You'll Be Assessed
Each lab step is verified before the group moves on — the instructor checks your show ip route output
You are assessed on reachability: can you ping your peer group, and can you explain the path
When a route is missing, a correct diagnosis counts for as much as a correct command
Checkpoint questions between sections are formative, not graded
Success criteria — by the close of this session each group can reach its peer group by static route, read its own routing table line by line, and say which code letter came from where.
Assessment
23

## Slide 24
SUMMARY
Key Takeaways
Routing is one question asked per packet: which entry in my table matches this destination?
Longest prefix match decides first. Administrative distance only breaks a tie between equal prefixes
Static routes are simple and stubborn; dynamic routes cost overhead and pay you back in failure recovery
IGPs run inside an autonomous system, BGP runs between them
Link-state protocols build a map and converge fast — which is why Lab 12 replaces your statics with OSPF
Summary
24

## Slide 25
INSTRUCTOR NOTES
Answer Key
Question 1 B
Longest prefix match comes first. /16 is more specific than /8, so administrative distance never gets a say.
Question 2 B
Static is 1, just behind a connected interface at 0.
Question 3 A
0.0.0.0 with mask 0.0.0.0 matches every destination — the gateway of last resort.
Question 4 C
BGP routes between autonomous systems. The other three are interior gateway protocols.
Question 5 B
Link-state routers flood link information and each builds its own full topology map.
Question 6 B
Equal prefix length, so distance decides: static at 1 beats OSPF at 110.
Answer Key — remove for student handout
25

## Slide 26
Questions?
Introduction to Routing — Network Infrastructure Workshop, SomNOG9
Based on original materials by the Network Startup Resource Center (NSRC, nsrc.org)
Licensed under Creative Commons Attribution-NonCommercial 4.0 International