## Slide 1
NETWORKING FUNDAMENTALS
Virtual LANs (VLANs)
Segmenting switched networks with IEEE 802.1Q
Layer 2 Switching Series

## Slide 2
LEARNING OBJECTIVES
By the End of This Session
Explain what a VLAN is, and why one broadcast domain per department beats one for the whole building
Configure an access port and a trunk, and say which frames are tagged on each
Describe what the 802.1Q tag adds to a frame, and what the native VLAN does differently
Choose between router-on-a-stick and an SVI, and justify the choice
Harden a switch against VLAN hopping — native VLAN, DTP, and unused ports
Learning Objectives
2

## Slide 3
OVERVIEW
Agenda
01
VLAN Fundamentals
What VLANs are, and why we segment networks
02
Trunking & Tagging
802.1Q, access vs trunk ports
03
Inter-VLAN Routing
Getting traffic between VLANs
04
VLAN Trunking Protocol
Propagating VLAN databases with VTP
05
Special VLANs & Security
Voice, management, and VLAN hopping
06
Design & Best Practices
Building a clean, secure VLAN plan
3
VLANs — Virtual LANs

## Slide 4
IN TODAY’S LAB
From Concept to Console
Labs 2–3: create VLAN 100 and VLAN 200 on SW1 and assign access ports to each
Lab 4: a DHCP pool per VLAN — VLAN 100 served from SW1, VLAN 200 from SW2
Lab 5: plug in and ping. Same VLAN works, different VLAN does not — that failure is the lesson
Lab 6: build the same VLANs on SW2 and ping across. It fails until the link between them is a trunk
Lab 7: only once inter-VLAN routing has failed do we add the SVI and let the switch route
Context only — VTP and private VLANs are covered for awareness. You will create VLANs by hand on both switches, which is what any careful production network does anyway.
In Today's Lab
4

## Slide 5
01 · VLAN FUNDAMENTALS
What Is a VLAN?
A VLAN (Virtual LAN) is a logical grouping of devices that behaves as its own separate broadcast domain — regardless of physical location or which switch a device is plugged into.
VLAN 10 — Sales
VLAN 20 — Engineering
VLAN 30 — Guest
One physical switch — three logically separate networks, defined purely by port configuration.
5
VLANs — Virtual LANs

## Slide 6
01 · VLAN FUNDAMENTALS
The Problem With Flat Networks
One Giant Broadcast Domain
Every broadcast — ARP, DHCP discovery — reaches every device on every switch.
No Traffic Isolation
HR, Finance, and Guest Wi-Fi all sit on the same segment with no separation.
Hard to Scale or Secure
As the network grows, performance degrades and access control becomes unmanageable.
VLANs solve this by carving one physical switch fabric into multiple logical broadcast domains — without running new cable.
6
VLANs — Virtual LANs

## Slide 7
01 · VLAN FUNDAMENTALS
Broadcast Domains: Before & After
WITHOUT VLANS
One flat broadcast domain — every port is identical, so every device hears every broadcast, regardless of department.
WITH VLANS
VLAN 10
VLAN 20
VLAN 30
Same physical switch — ports are grouped into separate VLANs, so traffic stays contained until a router forwards it between them.
7
VLANs — Virtual LANs

## Slide 8
01 · VLAN FUNDAMENTALS
Why Use VLANs?
Security
Sensitive traffic (Finance, HR) is isolated from general users and guests by default.
Performance
Smaller broadcast domains mean less flooding and less wasted bandwidth.
Flexibility
Group users logically (by team or function) instead of by physical location.
Simplified Management
Moves, adds, and changes happen through configuration, not recabling.
8
VLANs — Virtual LANs

## Slide 9
01 · VLAN FUNDAMENTALS
VLAN Membership Methods
Port-Based (Static)
Each switch port is manually assigned to a VLAN. Simple, predictable, and the most common method.
MAC-Based (Dynamic)
VLAN membership follows a device's MAC address via a mapping database, regardless of port.
Protocol-Based
Membership is determined by Layer 3 protocol or subnet — rare in modern networks.
9
VLANs — Virtual LANs

## Slide 10
01 · VLAN FUNDAMENTALS
VLAN IDs & Ranges
The 802.1Q tag reserves 12 bits for the VLAN ID, giving a theoretical range of 0–4095 — but not all of it is usable.
0 & 4095
Reserved
Reserved by the standard — not usable for configuration
1
Default VLAN
Exists automatically on every switch; cannot be deleted
2 – 1001
Normal Range
Standard VLANs, stored in vlan.dat, VTP-synchronized
1006 – 4094
Extended Range
For large networks; support varies by VTP version
10
VLANs — Virtual LANs

## Slide 11
01 · VLAN FUNDAMENTALS
Default VLAN vs. Native VLAN
Default VLAN (VLAN 1)
Every switch port belongs to VLAN 1 out of the box. It also carries control-plane traffic like CDP and STP by default — best practice is to move user data off it.
Native VLAN
On an 802.1Q trunk, the native VLAN's traffic is sent untagged. Mismatched native VLANs between two switches is a common (and risky) misconfiguration.
11
VLANs — Virtual LANs

## Slide 12
01 · VLAN FUNDAMENTALS
Common Types of VLANs
Data VLAN
Carries regular user-generated traffic — the most common VLAN type.
Voice VLAN
Dedicated to IP phone traffic, prioritized for latency-sensitive QoS.
Management VLAN
Carries traffic for switch/router administration — SSH, SNMP, HTTPS.
Native VLAN
Carries untagged traffic across a trunk link.
Default VLAN
VLAN 1 — active on every port unless explicitly reassigned.
Black-Hole VLAN
An unused VLAN assigned to disabled or unused ports for isolation.
12
VLANs — Virtual LANs

## Slide 13
CHECK YOUR UNDERSTANDING
Checkpoint 1 — VLANs and Tagging
QUESTION 1
Two PCs on the same switch, in different VLANs, cannot ping each other. Why?
A. The cable is faulty
B. They are separate broadcast domains and need a Layer 3 device
C. The switch has no MAC table
D. VLANs block ICMP by default
QUESTION 2
On an 802.1Q trunk, which frames cross the link untagged?
A. None — every frame is tagged
B. Frames in the native VLAN
C. Frames in VLAN 1 only
D. Broadcast frames only
QUESTION 3
How many bits does the 802.1Q tag give the VLAN ID?
A. 8 bits
B. 12 bits
C. 16 bits
D. 32 bits
Checkpoint
13

## Slide 14
02
Trunking & Tagging
Carrying multiple VLANs across a single link

## Slide 15
02 · TRUNKING & TAGGING
What Is a Trunk Link?
A trunk link carries traffic for multiple VLANs over a single physical connection — typically between switches, or between a switch and a router.
Switch A
Switch B
TRUNK
VLAN 10
VLAN 20
VLAN 30
Tagged frames for VLANs 10, 20, and 30 all ride the same cable, distinguishable end to end by their 802.1Q tag.
15
VLANs — Virtual LANs

## Slide 16
02 · TRUNKING & TAGGING
Access Ports vs. Trunk Ports
Aspect
Access Port
Trunk Port
Carries
Traffic for exactly one VLAN
Traffic for multiple VLANs
Tagging
Frames are untagged
Frames are 802.1Q tagged (except native)
Typical use
End devices — PCs, printers, phones*
Switch-to-switch, switch-to-router links
Configuration
switchport mode access
switchport mode trunk
* A phone port is often a hybrid: access for data, tagged for a separate voice VLAN.
16
VLANs — Virtual LANs

## Slide 17
02 · TRUNKING & TAGGING
IEEE 802.1Q Frame Tagging
802.1Q inserts a 4-byte tag between the source MAC address and the EtherType/Length field of an Ethernet frame.
Dest. MAC
Src. MAC
802.1Q Tag
EtherType
Payload
FCS
The tag adds: Tag Protocol ID (TPID), Priority Code Point (PCP), Drop Eligible Indicator (DEI), and the 12-bit VLAN ID (VID).
17
VLANs — Virtual LANs

## Slide 18
02 · TRUNKING & TAGGING
Inside the 802.1Q Tag
Field
Size
Purpose
TPID
16 bits
Tag Protocol ID — identifies the frame as 802.1Q tagged (0x8100)
PCP
3 bits
Priority Code Point — maps to 802.1p QoS class of service
DEI
1 bit
Drop Eligible Indicator — flags frames eligible to drop under congestion
VID
12 bits
VLAN Identifier — the actual VLAN number, 0–4095
18
VLANs — Virtual LANs

## Slide 19
02 · TRUNKING & TAGGING
Native VLAN & Untagged Traffic
Frames belonging to the native VLAN cross a trunk without a tag. If both ends don't agree on which VLAN is native, traffic can leak between VLANs.
Keep it consistent
Configure the same native VLAN on both ends of every trunk.
Use an unused VLAN
Dedicate an unused VLAN as native so no real data ever rides untagged.
Tag everything (802.1Q)
Some designs force-tag the native VLAN too, closing the gap entirely.
19
VLANs — Virtual LANs

## Slide 20
03
Inter-VLAN Routing
Because VLANs alone can't talk to each other

## Slide 21
03 · INTER-VLAN ROUTING
Why Do We Need Inter-VLAN Routing?
VLANs are separate Layer 3 subnets and separate broadcast domains. A switch alone cannot route between them — that requires Layer 3 forwarding, from a router or a Layer 3 switch.
Router-on-a-Stick
A single router interface, subdivided into logical sub-interfaces — one per VLAN.
Layer 3 Switch (SVI)
Switch Virtual Interfaces route between VLANs directly in hardware, at line rate.
21
VLANs — Virtual LANs

## Slide 22
03 · INTER-VLAN ROUTING
Router-on-a-Stick
A single physical link connects a router to a trunk port. The router creates a logical sub-interface for each VLAN, each with its own IP and 802.1Q tag.
Router
Trunk
(Gi0/0.10, .20, .30)
Switch (trunk port)
VLAN 10
VLAN 20
VLAN 30
Simple and low-cost but the single trunk link can become a bandwidth bottleneck as inter-VLAN traffic grows.
22
VLANs — Virtual LANs

## Slide 23
03 · INTER-VLAN ROUTING
Layer 3 Switch & SVIs
A multilayer switch creates a Switch Virtual Interface (SVI) for each VLAN — a virtual routed interface with its own IP address, no external router needed.
SVI: VLAN 10
10.10.0.1/24
interface Vlan10
SVI: VLAN 20
10.20.0.1/24
interface Vlan20
SVI: VLAN 30
10.30.0.1/24
interface Vlan30
Routes at hardware (ASIC) speed — the preferred design for modern campus and data center networks.
23
VLANs — Virtual LANs

## Slide 24
03 · INTER-VLAN ROUTING
Router-on-a-Stick vs. Layer 3 Switch
Aspect
Router-on-a-Stick
Layer 3 Switch (SVI)
Performance
Limited by one trunk link's bandwidth
Routes at wire speed in hardware
Cost
Reuses an existing router
Requires a Layer 3-capable switch
Scalability
Struggles as VLAN count/traffic grows
Scales well for campus and data center use
Best fit
Small networks, branch offices
Enterprise campus and core networks
24
VLANs — Virtual LANs

## Slide 25
CHECK YOUR UNDERSTANDING
Checkpoint 2 — Routing and Security
QUESTION 4
What is the main drawback of router-on-a-stick?
A. It cannot carry more than two VLANs
B. One trunk link becomes the bandwidth bottleneck
C. It requires VTP
D. It cannot use 802.1Q tagging
QUESTION 5
An attacker plugs a laptop into an access port and negotiates a trunk. What is this?
A. Double tagging
B. Switch spoofing
C. MAC flooding
D. ARP poisoning
QUESTION 6
Which single change does most to prevent that attack?
A. Enable VTP on every switch
B. Disable DTP and set access ports explicitly to access mode
C. Move every port into VLAN 1
D. Increase the trunk bandwidth
Checkpoint
25

## Slide 26
04
VLAN Trunking Protocol
Keeping every switch's VLAN database in sync

## Slide 27
04 · VLAN TRUNKING PROTOCOL
What Is VTP?
VTP (VLAN Trunking Protocol) is a Cisco protocol that distributes VLAN configuration across all switches in a domain, so VLANs only need to be created once.
One source of truth
Add a VLAN on one server switch — every switch in the domain learns it automatically.
Revision-numbered
Each update carries a higher configuration revision number so switches know what's newest.
Domain-scoped
Switches only exchange VTP updates if they share the same VTP domain name and password.
27
VLANs — Virtual LANs

## Slide 28
04 · VLAN TRUNKING PROTOCOL
VTP Modes
Server
Can create, modify, and delete VLANs. Advertises changes to the rest of the domain. Default mode.
Client
Receives and forwards VTP updates but cannot create or modify VLANs locally.
Transparent
Ignores domain updates and keeps its own local VLAN database — still forwards VTP frames it receives.
28
VLANs — Virtual LANs

## Slide 29
04 · VLAN TRUNKING PROTOCOL
VTP Versions & Pruning
Version
Key Capability
VTP v1
Baseline VLAN propagation; normal range only
VTP v2
Adds Token Ring VLAN support and consistency checks
VTP v3
Supports extended range VLANs and private VLANs
VTP Pruning
Automatically stops sending a VLAN's broadcast/multicast/unknown-unicast traffic down trunks that lead to switches with no ports in that VLAN — reducing unnecessary flooding.
29
VLANs — Virtual LANs

## Slide 30
05
Special VLANs & Security
Voice, management, and defending against VLAN hopping

## Slide 31
05 · SPECIAL VLANS & SECURITY
Voice VLAN & Management VLAN
Voice VLAN
Separates VoIP signaling/media from data traffic
Enables QoS prioritization for low-latency voice
Typically tagged on an otherwise access port
Management VLAN
Carries SSH, SNMP, and HTTPS admin traffic
Should never be VLAN 1 or a user data VLAN
Restrict access with ACLs on the SVI
31
VLANs — Virtual LANs

## Slide 32
05 · SPECIAL VLANS & SECURITY
VLAN Hopping Attacks
Switch Spoofing
An attacker's device negotiates trunking (DTP) with the switch, gaining access to all VLANs carried on that trunk.
Double Tagging
The attacker adds two 802.1Q tags; the outer tag is stripped at the first switch, letting the inner tag reach a different VLAN.
Both exploit default, permissive trunking behavior — which is exactly why hardening access ports matters.
32
VLANs — Virtual LANs

## Slide 33
05 · SPECIAL VLANS & SECURITY
Mitigating VLAN Hopping
Disable auto-trunking (DTP) — set unused/access ports to switchport nonegotiate
Explicitly set access ports to access mode, never leave them to negotiate
Change the native VLAN off VLAN 1 and off any data VLAN
Tag the native VLAN on trunks where supported, to remove the untagged gap
Prune unused VLANs from trunks so they cannot carry attacker traffic
Move unused ports to a dedicated black-hole VLAN and administratively shut them
33
VLANs — Virtual LANs

## Slide 34
05 · SPECIAL VLANS & SECURITY
Private VLANs (PVLANs)
A Private VLAN splits one primary VLAN into isolated secondary VLANs — useful when hosts need internet access but must not see each other (e.g. hotel or hosting networks).
Promiscuous
Can communicate with every port in the primary VLAN — typically the router/gateway port.
Isolated
Can only communicate with promiscuous ports — completely cut off from other secondary ports.
Community
Can communicate with each other and with promiscuous ports, but not with isolated ports.
34
VLANs — Virtual LANs

## Slide 35
06 · DESIGN & BEST PRACTICES
A Basic VLAN Configuration
A minimal Cisco IOS example: create a VLAN, assign an access port, and build a trunk.
Switch(config)# vlan 10
Switch(config-vlan)# name Sales
Switch(config)# interface fastEthernet 0/1
Switch(config-if)# switchport mode access
Switch(config-if)# switchport access vlan 10
Switch(config)# interface gigabitEthernet 0/1
Switch(config-if)# switchport mode trunk
Switch(config-if)# switchport trunk native vlan 999
35
VLANs — Virtual LANs

## Slide 36
06 · DESIGN & BEST PRACTICES
VLAN Design Best Practices
Plan before you build
Map VLANs to function (Data, Voice, Mgmt) — not to physical location — before configuring anything.
Use a consistent numbering scheme
e.g. VLAN 1X = Site 1, 2X = Site 2, so IDs are predictable across the network.
Leave room to grow
Reserve blocks of VLAN IDs for future departments or sites rather than numbering sequentially.
Isolate management traffic
Keep admin access on its own VLAN, off VLAN 1, protected by ACLs.
36
VLANs — Virtual LANs

## Slide 37
06 · DESIGN & BEST PRACTICES
Advantages & Limitations
Advantages
Segments broadcast domains without new cabling
Improves security by isolating sensitive traffic
Groups users logically instead of by location
Scales cleanly as the organization grows
Limitations
Requires a router or L3 switch for inter-VLAN traffic
Misconfigured trunks/native VLANs open security gaps
VTP mistakes can wipe VLAN databases domain-wide
Adds operational complexity vs. a flat network
37
VLANs — Virtual LANs

## Slide 38
ASSESSMENT
How You'll Be Assessed
Each lab step is verified before the group moves on — the instructor checks your show vlan brief output
You are assessed on the ping that works and the ping that does not, and on explaining both
When a cross-switch ping fails, a correct diagnosis counts for as much as a correct command
Checkpoint questions between sections are formative, not graded
Success criteria — by the close of this session each group has VLAN 100 and 200 live on both switches, a working trunk between them, hosts getting DHCP in the right VLAN, and can explain why an SVI was needed.
Assessment
38

## Slide 39
Key Takeaways
VLANs segment broadcast domains
One physical switch fabric becomes many logical networks.
Trunks carry many VLANs
802.1Q tags each frame so switches know which VLAN it belongs to.
Routing bridges VLANs
Router-on-a-stick or an L3 switch (SVI) moves traffic between them.
Design and secure deliberately
Consistent numbering, protected management VLANs, and hardened trunks prevent VLAN hopping.
35
VLANs — Virtual LANs

## Slide 40
INSTRUCTOR NOTES
Answer Key
Question 1 B
A VLAN is its own broadcast domain and its own subnet. Crossing between them is Layer 3 work.
Question 2 B
Native VLAN traffic crosses a trunk untagged — which is why both ends must agree on it.
Question 3 B
The VID field is 12 bits, giving 0–4095, of which 1–4094 are configurable.
Question 4 B
All inter-VLAN traffic hairpins through one physical link, so it saturates as VLANs grow.
Question 5 B
Switch spoofing: the attacker negotiates DTP and receives every VLAN on the trunk.
Question 6 B
Turning off DTP and pinning ports to access mode removes the negotiation the attack depends on.
Answer Key — remove for student handout
40

## Slide 41
Thank You
Questions about VLANs?