## Slide 1
NETWORK INFRASTRUCTURE WORKSHOP · 2026 EDITION
Other Layer-2 Features
Link Aggregation, Rapid & Multiple Spanning Tree, and Modern Switch Design
Updated with current IEEE standards, MLAG/vPC, EVPN-VXLAN, and real vendor examples

## Slide 2
AGENDA
What We'll Cover
Link Aggregation & MLAG
Bundling links for capacity and resilience — across one switch or two
Rapid Spanning Tree (802.1w)
Fast, loop-free convergence for redundant topologies
Multiple Spanning Tree (802.1s)
Per-VLAN topologies for genuine load balancing
Modern Data Center Fabrics
Where large-scale designs are heading beyond spanning tree
Switch Configuration Advice
Management, monitoring, and documentation done right
Other Layer-2 Features
2

## Slide 3
LINK AGGREGATION
Bundling Links for Capacity & Resilience
Also known as port bundling, link bundling, or (on Cisco gear) EtherChannel
Combine multiple physical links into one logical link for more bandwidth and fault tolerance
LACP is the standardized negotiation protocol — originally IEEE 802.3ad, now consolidated into IEEE 802.1AX-2014, the current governing standard for link aggregation
Vendor implementations: Cisco EtherChannel/Port-Channel, Juniper “ae” interfaces, Arista Port-Channel
Real-World Example
A server with dual 25 GbE NICs forms an LACP bundle to a Cisco Nexus 93180YC-EX, delivering 50 Gbps of active-active bandwidth with automatic failover — the modern equivalent of the 2×100 Mbps bundles common a decade ago.
Cloud and enterprise data centers now routinely bundle 4×100 GbE links between leaf switches and spine switches for 400 Gbps of aggregate uplink capacity.
Link Aggregation
3

## Slide 4
LACP OPERATION
How Two Switches Negotiate a Bundle
Switch A
Switch B
2 × 25 GbE + LACPDUs
Switch A
Switch B
Logical
50 Gbps link
Switches send LACPDU (Link Aggregation Control Protocol Data Unit) packets identifying themselves and each port's capabilities
Once negotiation matches, they automatically build the logical aggregated link and begin forwarding traffic across all members
Each port is configured as active (initiates negotiation) or passive (only responds)
If a member link fails, LACP automatically removes it from the bundle and keeps forwarding over the remaining links — no manual intervention needed
Link Aggregation
4

## Slide 5
LOAD BALANCING
Distributing Traffic Across a LAG
Bundled links distribute frames using a hashing algorithm, typically based on:
  Source and/or destination MAC address
  Source and/or destination IP address
  Source and/or destination L4 port numbers (“5-tuple” hashing)
Modern switches (Cisco Nexus, Arista EOS, Juniper Junos) default to 5-tuple hashing for far better entropy than MAC-only hashing used historically
A handful of very large “elephant” flows can still ride a single member link — always choose the hash mode that gives the most distribution for your traffic mix
Real-World Example
A 4×100 GbE spine-to-leaf bundle carrying thousands of small microservice flows balances evenly under 5-tuple hashing.
A single large iSCSI backup or VM migration flow, however, still rides just one member link no matter the hash — which is why high-throughput fabrics increasingly favor ECMP routing over simple Layer-2 LAGs.
Link Aggregation
5

## Slide 6
MODERN EXTENSION
MLAG & vPC — Cross-Chassis LAG
Standard LACP only bundles links terminating on ONE physical switch
Multi-Chassis Link Aggregation (MLAG) lets a device bundle links across TWO physical switches that appear as a single logical partner
Removes the single point of failure a whole-chassis outage would otherwise cause
Known by different names per vendor: Cisco Nexus vPC, Arista MLAG, Juniper MC-LAG, Aruba/HPE VSX
Switch A
Switch B
Peer link
Server
Server sees ONE logical port-channel
Real-World Example
Two Cisco Nexus 93180YC-EX switches form a vPC domain so a VMware ESXi host can uplink one NIC to each switch as a single active-active port-channel. If Switch A reboots for a firmware upgrade, traffic keeps flowing through Switch B with zero LACP renegotiation on the host.
Link Aggregation
6

## Slide 7
IEEE 802.1W · NOW PART OF 802.1Q
Rapid Spanning Tree Protocol (RSTP)
Backward-compatible with classic Spanning Tree (802.1D)
Convergence is much faster — seconds instead of 30–50 seconds — because switches communicate interactively rather than waiting on timers
Edge ports (access ports with no other switches attached) skip straight to the forwarding state
If a BPDU is ever received on an edge port, it immediately reverts to a normal, loop-checked port — protecting against accidental loops
Since 2011, RSTP's behavior has been folded directly into the IEEE 802.1Q standard rather than a separate amendment
Failover Convergence Time
802.1D (STP)
30–50 seconds
802.1w (RSTP)
< 1 second
Rapid Spanning Tree
7

## Slide 8
FAST CONVERGENCE
Port Roles & the Sync Handshake
Root Port
Best path toward the root bridge (same concept as classic STP)
Designated Port
Forwards for its segment (same concept as classic STP)
Alternate Port
Backup port with an alternate path to the root
Backup Port
Redundant path to a segment another port already serves
Root
Switch 1
Switch 2
Switch 3
Proposal ↓ / Agreement ↑
Root proposes each downstream link; once a switch agrees, it cascades the same handshake further down — only that branch briefly blocks, not the whole network.
Real-World Example
On a 3-tier campus network (core – distribution – access) with redundant uplinks, RSTP typically re-converges a failed link in under 1 second — versus 30+ seconds on legacy 802.1D — keeping VoIP calls and video conferencing from dropping.
Rapid Spanning Tree
8

## Slide 9
IEEE 802.1S · NOW PART OF 802.1Q
Multiple Spanning Tree Protocol (MSTP)
Backward-compatible with 802.1D and interoperable with RSTP
Runs a separate spanning-tree topology per group of VLANs — an “MST Instance” (MSTI)
Different topologies per instance let you load-balance across redundant uplinks instead of leaving one link idle
A particular VLAN maps to exactly one MSTI
Root: VLAN A
Root: VLAN B
Switch
VLAN A
VLAN B
Two active topologies share the same physical links — each VLAN group takes a different logical path to its own root
Multiple Spanning Tree
9

## Slide 10
MULTIPLE SPANNING TREE
Regions, CST & IST
MST Region
  Switches belong to the same region only if they share an identical MST configuration name, revision number, and VLAN-to-instance mapping
  A digest of these attributes rides inside every BPDU for fast comparison — one region is usually sufficient
Common Spanning Tree (CST)
  Defined in IEEE 802.1Q — connects separate MST regions and any legacy 802.1D switches into a single loop-free tree
Internal Spanning Tree (IST)
  Instance 0, always present on an MSTP switch — represents the whole region as a single virtual bridge to the CST outside
MST Region 1
(IST)
MST Region 2
(IST)
802.1D switch
Common Spanning Tree (CST) ties every region — and any legacy switch — into one loop-free tree, regardless of VLAN or region count
Multiple Spanning Tree
10

## Slide 11
BEST PRACTICES
Designing an MST Deployment
1
Map VLANs to instances that mirror your real forwarding paths
2
Assign a different root and alternate-root switch to each instance for genuine load sharing
3
Keep every switch's region name, revision number, and VLAN mapping identical
4
Leave instance 0 (the IST) free of VLAN assignments
Modern Tip
Most vendor platforms today (Cisco IOS-XE, Aruba AOS-CX, Juniper Junos) default to MST rather than legacy PVST+ for new deployments, since it scales far better once a network has hundreds of VLANs.
Multiple Spanning Tree
11

## Slide 12
LATEST TECHNOLOGY
Where Layer-2 Design Is Headed
Large data centers increasingly avoid STP-blocked links entirely by moving to a routed Layer-3 leaf-spine fabric
EVPN-VXLAN (RFC 7432 / RFC 8365) builds a virtual Layer-2 overlay on top of that routed IP underlay, using BGP — not spanning tree — to prevent loops, so every uplink stays active
Campus and branch networks still rely heavily on RSTP/MSTP, so both skill sets remain essential for a working network engineer
Real-World Example
Fabrics built on Cisco ACI, Arista CloudVision, or Juniper Apstra run EVPN-VXLAN so that all spine–leaf links forward traffic simultaneously with ECMP — something classic spanning tree, by design, could never do.
Modern Data Center Fabrics
12

## Slide 13
CASE STUDY
Putting It Together: A Campus Network
Core A
Core B
MLAG peer link
Dist. Bldg 1
Dist. Bldg 2
Dist. Bldg 3
Access SW
Solid = MST Instance 1 (Data VLAN, root = Core A) · Dashed = MST Instance 2 (Voice VLAN, root = Core B)
Core: two Cisco Catalyst 9500 switches paired via StackWise Virtual act as one logical root
Distribution: each building switch uses a 2×10G LACP/MLAG uplink to both core switches for redundancy
VLANs: the Data VLAN is pinned to Core A as MST root, the Voice VLAN to Core B — so both uplinks stay busy instead of one sitting idle
Real-World Design
13

## Slide 14
SWITCH CONFIGURATION ADVICE
Network Management, Updated
Monitoring
SNMP traps & syslog, centralized on a log server
Streaming telemetry (gNMI/gRPC) increasingly complements SNMP for near real-time visibility on modern platforms
Track spanning-tree changes, duplex mismatches, and wiring problems automatically
Open-source stacks in wide use today: LibreNMS or Zabbix, plus Prometheus + Grafana for dashboards
Configuration & Discovery
Back up configs and detect changes with Oxidized (RANCID's modern successor)
Or manage configs as code with Ansible + Git for versioned, auditable changes
Enable LLDP (vendor-neutral) alongside or instead of CDP to map how switches connect to each other and other devices
Collect forwarding tables via SNMP or gNMI to locate a MAC address quickly
Switch Configuration Advice
14

## Slide 15
SWITCH CONFIGURATION ADVICE
Documentation That Scales
Name switches by location and role, not just a sequence number — a good scheme encodes site, floor, and function at a glance
Track physical location, rack position, and cable patching in a single source of truth rather than scattered spreadsheets
Modern teams use a DCIM/IPAM platform such as NetBox or Device42 to centralize IPs, VLANs, cable maps, and rack elevations
Document every edge-port connection — room, jack, and device — and keep it in Git or NetBox so changes are reviewed and versioned, not just remembered
Example Naming Convention
Mog
Site (city)
hq
Building
fl3
Floor 3
dist
Role
sw01
Unit 01
Switch Configuration Advice
15

## Slide 16
SUMMARY
Key Takeaways
LAG & MLAG
Give you capacity and resilience, even across two chassis
RSTP
Delivers fast, simple convergence for redundant links
MSTP
Adds real load-balancing across VLANs at scale
EVPN-VXLAN
Goes further in the data center — but RSTP/MSTP remain the backbone of campus networks
Summary
16

## Slide 17
Questions?
Other Layer-2 Features — Network Infrastructure Workshop, 2026 Edition
Based on original materials by the Network Startup Resource Center (NSRC, nsrc.org)
Licensed under Creative Commons Attribution-NonCommercial 4.0 International