## Slide 1
NETWORK INFRASTRUCTURE WORKSHOP
Introduction to OSPF
Open Shortest Path First — link-state routing for IP networks
Updated Edition — September 2026
Updated Edition — September 2026
This document builds on original work by the Network Startup Resource Center (NSRC, nsrc.org) and SomNOG

## Slide 2
DEFINITION
OSPF
Open Shortest Path First — a link-state Interior Gateway Protocol (IGP) for routing within an autonomous system
“Open”
  An open, vendor-neutral standard
  Developed by the IETF OSPF Working Group; the original design was published as RFC 1247 (1991), since superseded
  Current base standard: OSPFv2, RFC 2328 (1998) — elevated to Internet Standard STD 54
“Shortest Path First”
  Edsger Dijkstra’s algorithm for computing a shortest-path tree through a graph
    Dijkstra, E. W. (1959). “A note on two problems in connexion with graphs.” Numerische Mathematik 1: 269–271
RFC 2328 remains the current OSPFv2 standard; see “Recent OSPF Developments” for the 2023 terminology update.
2

## Slide 3
PROTOCOL FAMILY
Link-State vs. Distance-Vector
Link-State
OSPF’s category of routing protocol
The other link-state protocol in wide use is IS-IS
Every node computes its own map of the network’s connectivity
Each router floods link-state information; all routers converge on the same topology
Distance-Vector
The other major type of IGP
Examples: RIP, and EIGRP
EIGRP originated as Cisco-proprietary, then was published as an open Informational spec, RFC 7868 (2016)
Each node shares its own view of the routing table with its neighbours, rather than raw topology
3

## Slide 4
NEIGHBOR DISCOVERY
The Hello Protocol
Routers with OSPF enabled look for neighbouring routers also running OSPF, using the “Hello” protocol
On OSPFv2, the Hello packet carries the subnet mask, the list of known neighbours, the “hello interval,” and the “router dead interval”
  Hello interval — how often the router sends Hellos
  Router dead interval — how long to wait before declaring a neighbour gone
  Hello interval, dead interval, and (on OSPFv2) subnet mask must match on both neighbours
OSPFv3 runs on a per-link, rather than per-subnet, basis — its Hello identifies neighbours by Interface ID and Router ID instead of an IPv4 subnet mask (RFC 5340)
When a neighbouring router responds with matching parameters, a neighbour relationship is formed
4

## Slide 5
RELATIONSHIPS
OSPF Neighbour Relationships
A relationship formed between selected neighbouring routers for the purpose of exchanging routing information is called an
  ADJACENCY
Not every pair of neighbouring routers becomes adjacent
  On multi-access networks (e.g. Ethernet), only selected routers form full adjacencies — see Designated Router, later
5

## Slide 6
INFORMATION EXCHANGE
OSPF Adjacencies
Once an adjacency is formed, neighbours share their link-state information
  Information is carried in a Link State Packet (LSP)
  LSPs sent to a neighbour are Link State Advertisements (LSAs)
New information received from neighbours is used to compute a fresh view of the network
On a link failure:
  New LSAs are flooded
  Routers recompute the routing table
Updated terminology (RFC 9454, Aug 2023): the Database Description exchange’s “Master/Slave” roles are now called “Leader/Follower” in both OSPFv2 (RFC 2328) and OSPFv3 (RFC 5340). This is a naming-only change — protocol behaviour is unaffected.
6

## Slide 7
SCALE
OSPF Across a Network
All routers across the network form neighbour relationships with their directly attached neighbours
Each router computes its own routing table
Once every router shares the same view of the network, the network has converged
IGP design is crucially important for scalability and rapid convergence
General rule: the fewer the prefixes, the faster the convergence
7

## Slide 8
HIERARCHY
OSPF Areas
OSPF has the concept of areas
  All networks must have an Area 0, the “backbone” / default area
  Areas exist to scale OSPF for large networks
  Most small-to-medium networks (up to roughly 300 routers) can comfortably run a single area
8

## Slide 9
VERSIONS
OSPFv2 and OSPFv3
OSPFv2 — IPv4
Carries IPv4 prefixes only
Defined in RFC 2328 (STD 54)
Terminology updated by RFC 9454 (2023): Leader/Follower
OSPFv3 — IPv6 (and more)
Originally for IPv6 prefixes; based on OSPFv2 concepts but a fully independent protocol instance
Documented in RFC 5340
Extended by RFC 5838 (2010) to carry multiple address families — including IPv4 — over OSPFv3
Also updated by RFC 9454 (2023): Leader/Follower
Configuration concepts and syntax remain very similar across the two versions, with subtle differences and improvements.
9

## Slide 10
TOPOLOGY TYPES
Links in OSPF
Two types of links in OSPF:
  Point-to-point link — only one other router on the link, forming a single point-to-point adjacency
  Multi-access network (e.g. Ethernet) — potentially many routers on the segment, with several possible adjacencies
OSPF on multi-access networks uses optimisations to aid scaling:
  Two routers are elected to originate the LSAs for the whole segment
  Called the “Designated Router” (DR) and “Backup Designated Router” (BDR)
  Other routers on the segment form full adjacencies only with the DR and BDR
10

## Slide 11
MULTI-ACCESS SCALING
Designated Router
There is ONE Designated Router per multi-access network
  Generates the network-link advertisement for the segment
  Assists in database synchronisation
  Scales OSPF for multi-access (Ethernet-type) networks
R1
Router
R2
Designated
Router
R3
Backup
Designated Router
R4
Router
11

## Slide 12
DR ELECTION
Selecting the Designated Router
Configured priority (per interface) — configure a high priority on the routers meant to be DR/BDR
Otherwise, priority is determined by the highest Router ID
  Router ID is a 32-bit value, in dotted-quad form
  Set manually, otherwise derived from a loopback interface’s IPv4 address, otherwise the highest active IPv4 address on the router
  Best practice: set router-id explicitly, so a link flap can’t silently change the elected DR
DR — higher Router ID via loopback
131.108.3.2
131.108.3.3
R1
R2
R1 Router ID = 144.254.3.5 (loopback)
R2 Router ID = 131.108.3.3 (no loopback)
12

## Slide 13
VERIFICATION
Adjacencies: Examples
To find adjacency state:
show ip[v6] ospf neighbor
Point-to-point link
Neighbor ID Pri State Dead Time Address Interface
10.10.15.236 0 FULL/- 00:00:35 10.10.15.16 Serial1/0
Multi-access link — FULL/BDR and FULL/DR: other routers adjacent to DR/BDR
Neighbor ID Pri State Dead Time Address Interface
10.10.15.225 1 FULL/BDR 00:00:35 10.10.15.2 FastEth0/0
10.10.15.226 1 FULL/DR 00:00:35 10.10.15.3 FastEth0/0
2WAY/DROTHER: neighbour seen, but not DR/BDR — no full adjacency needed
Neighbor ID Pri State Dead Time Address Interface
10.10.15.227 1 2WAY/DROTHER 00:00:35 10.10.15.4 FastEth0/0
Command syntax and states shown are current on Cisco IOS/IOS-XE; other vendors expose equivalent state via their own show commands.
13

## Slide 14
CONFIGURATION
OSPF on Cisco IOS
Starting OSPFv2 (IPv4):
router ospf 42
Starting OSPFv3 (IPv6):
ipv6 router ospf 42
“42” is the process ID, unique to the router
  Gives the possibility of running multiple OSPF instances on one router
  The process ID is locally significant only — it is not passed between routers in an AS
  Some ISPs configure the process ID to match their BGP Autonomous System Number, as a convention
  Note: this syntax is current for Cisco IOS/IOS-XE; IOS-XR and NX-OS accept a named or numbered OSPF process tag, and other vendors (Juniper, Arista, Nokia) use their own CLI/config-model syntax for the same concepts
14

## Slide 15
CONFIGURATION
OSPF on Cisco IOS — Forming Neighbours
OSPF must be activated on the interface where a neighbour relationship is desired:
interface POS 4/0
ip address 192.168.1.1 255.255.255.252
ip ospf 42 area 0
!
router ospf 42
passive-interface default
no passive-interface POS 4/0
!
“passive-interface default” suppresses Hellos everywhere, then “no passive-interface” re-enables them only where adjacencies are wanted — still the recommended pattern for controlling exactly where OSPF forms neighbours
15

## Slide 16
PATH SELECTION
OSPF Interface Costs
Cisco IOS sets interface cost automatically: cost = 10⁸ / interface bandwidth
  That default (100 Mbps reference bandwidth) was fine when 100 Mbps was fast
Many operators set their own interface-cost strategy
ip ospf cost 100
Sets interface cost to 100
Still true today: OSPF chooses the lowest-cost path through a network, and load-balances across equal-cost paths to the same destination. Needs updating for modern links: with the default 100 Mbps reference bandwidth, cost = 10⁸/bandwidth rounds to the same minimum value (1) for every interface at or above 100 Mbps — so 1G, 10G, 100G, and 400G links all look identical to SPF by default. Set a consistent, higher “auto-cost reference-bandwidth” (e.g. in the hundreds of thousands of Mbps) on every router in the domain, or assign “ip ospf cost” explicitly, to keep path selection meaningful on today’s high-speed links.
16

## Slide 17
WORKED EXAMPLE
OSPF Metric Calculation
Best path / lowest cost = 60 (via R1 → R3 → R4)
Server
Client
R1
R2
R3
R4
5 Mbps — cost 20
2 Mbps — cost 50
2 Mbps — cost 50
10 Mbps — cost 10
R1→R2→R4 = 20+50 = 70. R1→R3→R4 = 50+10 = 60 — lower cost, so OSPF installs this path only.
17

## Slide 18
WORKED EXAMPLE
OSPF Metric Calculation
Equal-cost paths = 70 each → OSPF load-balances across both
Server
Client
R1
R2
R3
R4
5 Mbps — cost 20
2 Mbps — cost 50
1.3 Mbps — cost 60
10 Mbps — cost 10
R1→R2→R4 = 20+50 = 70. R1→R3→R4 = 60+10 = 70 — equal cost, so OSPF installs and load-balances across both paths.
18

## Slide 19
WHAT'S NEW
Recent OSPF Developments
RFC 9454 (Aug 2023) — Inclusive-language terminology update
  Renames “Master/Slave” to “Leader/Follower” across OSPFv2 (RFC 2328), OSPFv3 (RFC 5340), and five related RFCs — no change to protocol behaviour
Segment Routing extensions — RFC 8665 (OSPFv2) and RFC 8666 (OSPFv3)
  Let OSPF advertise SR-MPLS Segment IDs so paths can be engineered without a separate signalling protocol; now widely deployed in service-provider and data-centre fabrics
IGP Flexible Algorithm (“Flex-Algo”) — RFC 9350 (2023)
  Lets OSPF (and IS-IS) compute extra, constraint-based paths — e.g. lowest latency — alongside standard shortest-path-first, still inside the same IGP
Segment Routing over IPv6 (SRv6) for OSPFv3 — ongoing IETF work
  Extends segment-routing capability natively into the IPv6 data plane for OSPFv3 domains
None of this changes OSPF’s core mechanics (Hello, flooding, SPF) — these are additive extensions operators opt into.
19

## Slide 20
CONCLUSION
Keep It Simple
OSPF is a link-state routing protocol — its core mechanics are unchanged since RFC 2328 (1998) and RFC 5340 (2008)
Quick and simple to get started, with a myriad of options and features covering almost any network topology
ISPs keep their OSPF design SIMPLE
Roughly 300 routers in a single area remains entirely feasible
Segment Routing and Flex-Algo extend OSPF for modern traffic-engineered, SDN-integrated networks — without changing that founding principle

## Slide 21
Questions?