## Slide 1
TECHNICAL WORKSHOP
Campus Network
Design & Operations
A practical guide for resilient, secure, and research-ready campus networks
Design principles • Architecture • Protocols • Operations • Security • Instrumentation
Prepared for research and education network practitioners
01

## Slide 2
Why Campus Network Design Matters
The network should enable learning, research, collaboration, and institutional services.
Research and education workloads
High-throughput data movement, real-time collaboration, cloud services, digital libraries, online exams, and HPC-style workloads.
Operational reality
Constrained budgets, mixed hardware, power interruptions, evolving buildings, and limited on-site technical staff.
Design objective
Build a network that remains understandable, monitorable, resilient, and scalable as demand grows.
The campus network must not become the bottleneck.
Support open, flexible access while keeping sensitive systems protected.
Separate traffic and failure domains so one issue does not affect the whole campus.
Use managed devices and telemetry to understand performance before users complain.
Plan growth in stages, with documented standards and clear decision points.
OUTCOME: A reference design you can adapt

## Slide 3
Workshop Roadmap
Six connected sections move from architecture through operations and discussion.
01
Core infrastructure design
Design principles, cabling, fiber, core and edge architecture
02
Equipment and protocols
Switching, routing, addressing, device selection, wireless
03
Core network operations
Capacity, change control, incident response, baselines
04
Campus security
Security zones, AUP, firewall placement, hardening
05
Instrumentation
Monitoring, telemetry, logging, configuration management
06
Networking roundtable
Scenario review, group decisions, action planning

## Slide 4
Reference Campus Scenario
We will use a realistic multi-building institution as a common design case.
Campus profile
6 buildings, 1 data centre, 1,200 users, student and staff Wi-Fi, internet-facing services, research traffic.
Business priorities
Availability, safe access to services, video collaboration, online learning, and predictable performance.
Technical constraints
Budget phased over 24 months. Existing copper plant is mixed. Fiber is available between most buildings.
REFERENCE ARCHITECTURE
Internet / NREN
Border + FW
Core A
Core B
Data Centre
Library
Faculty
Labs
Admin
Dorms
Innovation
Task: Design this campus in a way that stays simple as it grows

## Slide 5
Campus Design Principles
Use these principles to guide every architecture decision.
1
Keep paths short
Reduce devices, hops, and hidden dependencies in common traffic paths.
2
Use hub-and-spoke topology
Connect buildings to a resilient core instead of chaining them together.
3
Route at security and fault boundaries
Use Layer 3 to create clear segmentation, policy, and failure containment.
4
Place shared services near the core
Locate data centre services where power, cooling, security, and resilient links exist.
5
Operate managed infrastructure
Choose devices that support inventory, configuration backup, telemetry, and alerts.

## Slide 6
Avoid Daisy Chaining: Build for Short, Predictable Paths
A campus that looks simple on paper can become hard to operate when buildings depend on adjacent buildings.
Preferred: hub-and-spoke campus backbone
Each building receives a direct fiber path to the core or a resilient aggregation point. A failure stays local, capacity is easier to plan, and troubleshooting is faster.
Core
Bldg A
Bldg B
Bldg C
Bldg D
Separate failure domains
Risky: daisy-chained backbone
One building becomes a transit point for another. A single fault, power issue, or overloaded link affects more users and increases time to isolate the cause.
Bldg A
Bldg B
Bldg C
Bldg D
Core
Single fault can affect multiple buildings

## Slide 7
Campus Architecture: Core, Aggregation, Access, and Services
A clear hierarchy improves resilience, policy enforcement, and operational visibility.
Perimeter
Internet edge, DDoS, firewall, external services
Core
Fast Layer 3 forwarding, inter-building routing, policy boundaries
Aggregation
Building aggregation, fiber termination, resilient uplinks
Access
User ports, PoE, VLANs, wireless APs, edge protection
Services
Identity, DNS/DHCP, applications, storage, monitoring
Principle: Use Layer 3 where you need control, isolation, and predictable recovery

## Slide 8
Core Network Reliability
The core supports the campus. Treat it as critical infrastructure.
Power
Dual UPS paths, generator support where available, surge protection, grounding and bonding.
Environment
Cooling, temperature monitoring, clean racks, secure access, documented patching.
Hardware
Redundant supervisors or core pair, diverse power feeds, spare optics, labeled uplinks.
Connectivity
Diverse fiber paths, resilient uplinks, routed redundancy, capacity headroom.
Core design decision test
If this component fails, how many buildings, users, and critical services become unavailable? Design first around the largest impact.
Identify and reduce single points of failure

## Slide 9
Where to Place Servers and Shared Services
Keep high-value services in a controlled environment and on dedicated routed segments.
Internet / NREN
Border Router
Firewall
Core Pair
Server Zone
Monitoring
Library
Faculty
Labs
Admin
ROUTED, PROTECTED, MONITORED
Do not place servers on the same unrestricted subnet as student or staff endpoints.
Create dedicated server, management, and monitoring zones.
Enforce policy at the firewall or routed security boundary, not with informal cabling decisions.

## Slide 10
Segmentation: Contain Broadcasts, Risk, and Operational Noise
A single campus-wide subnet removes useful security and troubleshooting boundaries.
Student Wi-Fi
10.20.0.0/16
Internet only, rate limits
Staff
10.30.0.0/16
Business systems, Internet
Research
10.40.0.0/16
High-throughput, controlled access
Servers
10.50.0.0/20
Restricted inbound policy
Management
10.60.0.0/20
Admin-only access
Design rule: Segment by trust, function, and operational need. Use VLANs for Layer 2 separation and Layer 3 or firewalls for policy enforcement.

## Slide 11
Design Lab 1: Draw the Core and Building Backbone
Apply the design principles to the reference campus before choosing equipment.
Team task
Place the core, border, data centre, and six buildings on a blank campus map.
Draw fiber paths and identify where diverse paths are justified.
Choose Layer 3 boundaries and name at least five routed segments.
List three single points of failure and a practical mitigation for each.
DELIVERABLE: ONE-PAGE DESIGN
Review criteria
1
Topology
Direct building paths, no accidental transit
2
Segmentation
Clear subnets and logical boundaries
3
Resilience
Power, fiber, hardware, and failure isolation
4
Operations
Managed devices and monitoring included

## Slide 12
Physical Infrastructure: MDF, IDF, and Structured Cabling
The cabling plant is part of the network. Poor pathways, labeling, or termination cause operational problems for years.
BUILDING CABLING MODEL
MDF
Main equipment room
IDF 1
IDF 2
IDF 3
Work areas
APs / phones
Cameras / IoT
Use fiber for MDF-to-IDF backbone links. Use standards-compliant copper horizontal cabling for endpoints and APs.
MDF standards
Secure room, clean power, UPS, cooling, grounding, documentation, structured patching, and access control.
IDF standards
Racks close to users, UPS where feasible, labeled patch panels, protected pathways, and uplinks sized for demand.
Cabling standards
Separate data from electrical power, respect bend radius, avoid tension, label both ends, and maintain accurate as-builts.

## Slide 13
Fibre Optics for the Campus Backbone
Fibre links should support capacity growth, resilient building connectivity, and clean fault isolation.
Single-mode fibre (SMF)
Best default for inter-building and long-distance campus backbone links. Supports high capacity and future growth.
Multi-mode fibre (MMF)
Useful for short in-building backbone links where existing plant and optics strategy support it.
Optics and connectors
Standardize connector type, optics compatibility, spare quantities, labeling, and cleaning procedures.
Fibre acceptance checklist
1
Pathway
Use protected ducts, trays, or conduit. Keep a route record.
2
Termination
Use labeled panels and clean connector practices.
3
Testing
Record insertion loss, polarity, and OTDR/OLTS test evidence.
4
Resilience
Where risk justifies it, use diverse paths or separate ducts.
Treat fibre test results, labels, and route drawings as handover deliverables

## Slide 14
Cabling Installation and Handover Checklist
A network installation is not complete until the physical layer is documented, tested, and maintainable.
1
Survey
Confirm routes, room locations, power, grounding, rack space, and future expansion.
2
Install
Use approved cable type, protected pathways, correct bend radius, and separation from power.
3
Terminate
Use labeled patch panels, proper strain relief, clean fibre end faces, and secure racks.
4
Test
Certify copper links. Capture fibre test results and document failed or marginal links.
5
Handover
Deliver as-built diagrams, port maps, labels, test records, spare inventory, and access procedures.
Handover test: another technician should be able to locate, identify, and test any link without guesswork

## Slide 15
01
Session 01 Quiz: Core Infrastructure Design
Multiple choice • Select one answer • Part 1 of 2
1
Which backbone model best reduces accidental building-to-building dependency?
A. Daisy chain B. Hub-and-spoke with direct fibre
C. One flat Wi-Fi subnet D. Guest-only tunnel
2
Where should routing normally be placed when policy and recovery matter?
A. Only at access ports B. Inside unmanaged switches
C. At security and fault boundaries D. Only at wireless APs
3
Why place servers in routed, protected, monitored zones?
A. To share student subnets B. To reduce power use
C. To apply clear access policy and visibility D. To avoid DNS design
Campus Network Design & Operations Workshop
15

## Slide 16
02
Campus Network Equipment and Protocols
Build a reliable Layer 2 and Layer 3 foundation, then select equipment that fits the design.
Campus Network Design & Operations Workshop

## Slide 17
Equipment Roles in a Campus Network
Choose the device based on its job in the architecture, not only port count or price.
Border router
Connects to ISP or NREN, routes external prefixes, applies routing policy.
Firewall
Enforces security zones, application policy, VPN, and controlled outbound access.
Core / L3 switch
High-speed campus routing, aggregation, equal-cost paths, service reachability.
Access switch
Connects users, phones, APs, cameras, and applies edge protection.
Wireless platform
AP management, RF policy, client segmentation, guest access, roaming.
Monitoring platform
Collects telemetry, logs, flow data, configuration state, and alerts.

## Slide 18
Choosing Campus Routers and Switches
Use a structured selection method. Avoid buying unmanaged devices for production networks.
Decision area
Questions to ask
Practical target
Capacity
What throughput, port speed, and growth headroom do we need?
1 Gb/s access, 10/25 Gb/s uplinks as demand requires
Resilience
How do we avoid a single power, supervisor, or uplink failure?
Redundant uplinks, hot-swappable power where justified
Operations
Can we monitor, backup, secure, and automate configuration?
SNMPv3, Syslog, NetFlow/IPFIX, API/SSH, config archive
Security
Can the platform enforce edge protection and access control?
802.1X, DHCP snooping, RA Guard, port-security, ACLs
Lifecycle
Will optics, software, support, and spares remain available?
Supported software train, documented warranty, spare optics
Rule: managed capability is a requirement, not a luxury

## Slide 19
Switching Foundation: VLANs, Trunks, and Routed Gateways
Use Layer 2 for local access. Use Layer 3 to move between segments.
ONE BUILDING
L3 Gateway
SVIs / routed links
Access Switch A
Access Switch B
VLAN 10
Students
VLAN 20
Staff
VLAN 30
Printers
VLAN 40
Faculty
VLAN 50
Voice
VLAN 60
APs
Trunks carry multiple VLANs between network devices. End-user ports should carry only the one VLAN they need.
VLAN design rules
Use a consistent numbering standard. Document VLAN purpose, subnet, gateway, DHCP scope, and security policy.
Trunk design rules
Allow only required VLANs. Use a dedicated native/unused VLAN. Disable dynamic trunking where practical.
Gateway design rules
Place the default gateway at a Layer 3 boundary. Route where policy, reliability, and troubleshooting need it.

## Slide 20
Spanning Tree: Prevent Layer 2 Loops Before They Stop the Campus
Redundant links are useful only when loop prevention and root placement are intentional.
Why STP exists
Ethernet frames have no built-in hop counter. A Layer 2 loop can flood traffic until users lose connectivity.
Root bridge placement
Make the core or distribution layer the STP root for the VLANs it serves. Do not leave this to election by default.
Design preference
Use routed links between major blocks where practical. Keep Layer 2 domains intentionally small.
STP EXAMPLE
Root Bridge
Distribution
Access A
Access B
Blocked backup path
Root: intentional • Backup: documented • Access ports: protected

## Slide 21
Layer 2 Protection Features
Secure the access edge where users and unmanaged devices connect.
BPDU Guard
Shuts down an access port that receives unexpected BPDUs.
Protects against accidental switch connections.
Root Guard
Prevents an access switch from becoming the STP root.
Keeps root placement under your control.
DHCP Snooping
Builds a trusted DHCP binding table and blocks rogue DHCP replies.
Protects clients from fake gateway/DNS offers.
Dynamic ARP Inspection
Validates ARP traffic against DHCP snooping bindings.
Reduces ARP spoofing on user VLANs.
IPv6 RA Guard
Blocks unauthorized IPv6 router advertisements at the access edge.
Prevents rogue default gateway announcements.
Port security / 802.1X
Limits device identity or requires authentication before access.
Reduces unauthorized physical access.

## Slide 22
Configuration Lab 2: VLANs, Trunks, STP, and Layer 2 Protections
Create a secure small-building access design in Packet Tracer or a lab switch environment.
1
Create VLANs
Students, Staff, Printers, Guest, and Management
2
Configure trunks
Allow only required VLANs between access and distribution
3
Set root bridge
Choose the distribution switch as primary root and define a backup root
4
Protect access ports
Apply PortFast, BPDU Guard, DHCP Snooping, and RA Guard where supported
5
Test failures
Connect a rogue switch, fake DHCP server, and unexpected router advertisement
SUCCESS CRITERIA
Correct VLAN membership, stable STP topology, no rogue services, and documented verification commands.

## Slide 23
Routing: Static, OSPF, and IS-IS
Choose the protocol based on scale, operations skills, policy requirements, and failure recovery needs.
Static routing
Best for a few stable paths, default routes, and tightly controlled links.
Strength: simple and deterministic.
Watch-out: manual changes do not scale.
OSPF
Common enterprise IGP with areas, fast convergence, IPv4 and IPv6 support.
Strength: familiar, broadly supported.
Watch-out: requires disciplined area design.
IS-IS
Link-state IGP often used by providers and large backbones.
Strength: scalable, clean Layer 2 adjacency model.
Watch-out: team familiarity matters.
Design rule: Use static routing for stable edges. Use an IGP inside the campus where multiple routed paths and fast recovery are needed.

## Slide 24
OSPF Campus Design
Keep the backbone stable and make area boundaries meaningful.
OSPF REFERENCE
Core A
Area 0
Core B
Area 0
Library
Area 10
Faculty
Area 20
Labs
Area 30
Area 0 carries core transit. Building or service blocks become non-backbone areas when the campus needs hierarchy and route summarization.
Design guideline
Use Layer 3 links between core and buildings. Summarize routes at clear boundaries where the platform supports it.
Operational guideline
Document router IDs, area IDs, network types, authentication, passive interfaces, and adjacency expectations.
Verification
Check neighbors, LSDB, routes, interface counters, and convergence behavior after a link failure.

## Slide 25
IPv4, IPv6, and Dual-Stack Deployment
Run both protocols in a controlled way while building IPv6 operational maturity.
1. Address plan
Reserve hierarchical IPv4 and IPv6 blocks by campus, building, service, and management plane.
2. Enable dual stack
Provide IPv4 and IPv6 on selected routed links, server zones, and pilot user VLANs.
3. Protect IPv6
Apply RA Guard, DHCPv6 Guard, IPv6 ACLs, logging, and management-plane controls.
4. Monitor both
Track IPv4 and IPv6 reachability, DNS records, flow data, and incident procedures equally.
Practical rule: IPv6 is not only “more addresses.” Treat it as a full operational stack with addressing, DNS, policy, logging, and troubleshooting procedures.

## Slide 26
Introduction to Campus Wireless
Wireless is an access layer service. It needs the same planning, segmentation, and monitoring as the wired network.
Wireless design decisions
Coverage and capacity based on room use, user density, and building materials.
RF channel plan, power settings, and roaming behavior.
SSID-to-VLAN mapping with staff, student, guest, and IoT separation.
Secure onboarding using 802.1X or managed credentials where feasible.
PoE budgets, uplink bandwidth, and controller or cloud management.
BUILDING FLOOR EXAMPLE
AP locations are driven by capacity and RF survey results, not by uniform spacing alone.

## Slide 27
Configuration Lab 3: Routed Campus and Dual Stack
Build a small campus with OSPF and dual-stack connectivity.
Core A
Core B
Building 1
Building 2
Server Zone
Tasks and checks
1. Configure IPv4 and IPv6 addresses on all routed links.
2. Enable OSPF for IPv4 and OSPFv3 or IPv6-capable routing for IPv6.
3. Use loopback interfaces and stable router IDs.
4. Verify dual-stack ping and traceroute between Building 1, Building 2, and Server Zone.
5. Shut one routed link, observe reconvergence, and record the result.
6. Apply a simple ACL to restrict student access to the management subnet.
Evidence: routing table, neighbor state, ping, traceroute, and failure test

## Slide 28
02
Session 02 Quiz: Equipment and Protocols
Multiple choice • Select one answer • Part 1 of 2
1
Why choose managed devices for production networks?
A. They are always cheaper B. They remove the need for design
C. They support monitoring, backup, security, automation D. They prevent every outage
2
Which trunk practice is safest?
A. Allow all VLANs B. Allow only required VLANs and use an unused native VLAN
C. Use the student VLAN as native D. Enable dynamic trunking everywhere
3
What does BPDU Guard do on an access port?
A. Shuts the port when unexpected BPDUs arrive B. Assigns IP addresses
C. Builds an ARP table D. Creates OSPF neighbors
Campus Network Design & Operations Workshop
29

## Slide 29
03
Best Practice Techniques in Core Network Operations
Keep the network available by measuring it, maintaining it, and recovering from issues in a controlled way.
Campus Network Design & Operations Workshop

## Slide 30
Core Operations Lifecycle
Reliable service comes from routine discipline, not only from high-end equipment.
1
Baseline
Document topology, addressing, hardware, software, services, and normal performance.
2
Monitor
Collect availability, latency, packet loss, utilization, environmental data, logs, and flow data.
3
Review
Check capacity trends, recurring incidents, configuration drift, and security events.
4
Change
Plan, test, approve, implement, verify, document, and prepare rollback.
5
Improve
Remove single points of failure, refresh lifecycle risks, and automate repetitive checks.
Operating principle: Every change should leave the network in a better documented and more observable state than before.

## Slide 31
Monitoring Stack: From Device Signals to Action
Use multiple data sources. No single tool explains every incident.
Network devices
Interface status, errors, CPU, memory, temperature, optical levels
Telemetry collectors
SNMPv3, streaming telemetry, Syslog, NetFlow/IPFIX, traps
Analytics and dashboards
Availability, traffic, latency, capacity, inventory, topology, service views
Operations workflow
Alert routing, ticketing, escalation, incident notes, post-incident action
Aim for actionable alerts, not a dashboard full of noise

## Slide 32
Capacity, Baselines, and Performance Management
You need normal behaviour before you can recognize abnormal behaviour.
Availability
Device, link, DNS, DHCP, authentication, and internet reachability
Performance
Latency, packet loss, jitter, interface utilization, Wi-Fi retries
Health
CPU, memory, temperatures, power supply, optical Rx/Tx, errors/discards
Security
Authentication failures, port violations, blocked traffic, config changes, anomalies
Baseline practice: record normal busy-hour utilization and latency. Start investigation when trends change, not only when a link goes down.

## Slide 33
Operational Controls: Change Management and Incident Response
Small process controls prevent repeat outages and shorten recovery time.
Change checklist
• Define the objective and expected outcome.
• Record affected services and dependencies.
• Prepare the implementation steps and verification tests.
• Define a rollback trigger and rollback steps.
• Get peer review or approval based on impact.
• Update documentation after the change.
Incident checklist
• Confirm impact and scope.
• Preserve useful logs and device state.
• Stabilize the service before optimizing.
• Communicate concise status updates.
• Record the root cause, contributing factors, and follow-up actions.
• Turn the lesson into a monitoring or design improvement.

## Slide 34
Operations Lab 4: Diagnose the Campus Before Users Call
Use a structured method to isolate a performance complaint.
1
Situation
Students report slow access to the digital library between 10:00 and 12:00.
2
Collect evidence
Check interface utilization, packet loss, Wi-Fi client counts, DNS response, and firewall sessions.
3
Form hypotheses
Congested uplink? RF capacity issue? DNS delay? Firewall policy? Server capacity?
4
Test one layer at a time
Compare wired vs wireless, local vs remote, IPv4 vs IPv6, and normal vs affected times.
5
Document outcome
Record the evidence, root cause, fix, and monitoring metric that would detect recurrence.

## Slide 35
03
Session 03 Quiz: Core Network Operations
Multiple choice • Select one answer • Part 1 of 2
1
What should start the core operations lifecycle?
A. Baseline normal state B. Replace all hardware
C. Disable alerts D. Wait for complaints
2
Why use multiple monitoring data sources?
A. It makes dashboards colourful B. It removes the need for tickets
C. No single tool explains every incident D. It replaces documentation
3
Which evidence helps confirm a Wi-Fi performance issue?
A. Rack colour B. Spare cable count
C. Software warranty only D. Retries, client counts, latency, packet loss
Campus Network Design & Operations Workshop
37

## Slide 36
04
Campus Security Implementation and Best Practices
Protect people, systems, and research data without blocking legitimate learning and collaboration.
Campus Network Design & Operations Workshop

## Slide 37
Security Architecture: Define Zones and Trust Boundaries
Security is strongest when policy follows the topology.
Internet
Firewall
Core
DMZ
Server
Staff
Student
Guest
Management
Zone principle
Group assets by trust and function. Every zone should have a defined security policy.
Policy principle
Permit explicitly required flows. Keep rules specific, documented, and reviewed.
Management principle
Use a dedicated management zone. Do not manage infrastructure from user networks.

## Slide 38
Firewall Placement: Where It Helps Most
Firewalls enforce policy at high-value boundaries. They are not a substitute for network design.
1
Internet perimeter
Protects inbound services, outbound policy, VPN, and egress visibility.
2
DMZ boundary
Separates public-facing systems from internal server networks.
3
Data centre / server zone
Controls access to institutional applications and sensitive data.
4
Guest Wi-Fi exit
Keeps guests isolated from internal networks and routes them to the internet.
5
Management zone
Restricts network-device administration to authorized administrators.
Do not place every internal VLAN behind a firewall without a clear risk and performance reason

## Slide 39
Acceptable Use Policies: The Human Layer of Campus Security
Policies set clear expectations for users, administrators, and institutional leaders.
Access
Who receives accounts, how access is approved, and what identity checks apply.
Responsible use
Rules for academic, research, administrative, and personal device usage.
Security responsibilities
Password/MFA expectations, reporting lost devices, and prohibited activities.
Data protection
How sensitive records, research data, backups, and cloud services must be handled.
Enforcement and review
How violations are handled, who owns policy updates, and when review happens.
A policy must be short enough to read, clear enough to apply, and owned by people who can update it.

## Slide 40
Security Configuration Baseline
Apply controls consistently across routers, switches, wireless, and management platforms.
Administration
AAA, named accounts, least privilege, MFA where supported, SSH only
Management plane
Dedicated management subnet, ACLs, out-of-band access, secure NTP, DNS, and SNMPv3
Logging
Central Syslog, time synchronization, authentication logs, configuration change logging
Edge ports
BPDU Guard, DHCP Snooping, ARP Inspection, RA Guard, 802.1X/port security
Lifecycle
Supported software, backups, vulnerability review, spare config and recovery plan

## Slide 41
Security Lab 5: Write a Zone Policy and Test It
Convert security design into explicit, verifiable access rules.
Student
Internet, learning platform, DNS/DHCP, selected library resources
Define ports, direction, logging, and owner
Staff
Internet, institutional applications, printer services, selected research services
Define ports, direction, logging, and owner
Guest
Internet only. No internal subnets.
Define ports, direction, logging, and owner
Management
Network devices, monitoring, backups, identity services
Define ports, direction, logging, and owner
DMZ
Public services only, tightly limited flows to internal dependencies
Define ports, direction, logging, and owner
Task: turn this matrix into an ACL or firewall policy, then test each allow/deny flow

## Slide 42
04
Session 04 Quiz: Campus Security
Multiple choice • Select one answer • Part 1 of 2
1
Why define security zones?
A. To make more VLAN names B. To group assets by trust and function with clear policy
C. To avoid routing D. To remove monitoring
2
Where do firewalls help most?
A. Between every access port B. Inside every AP
C. At high-value boundaries D. Only in the server rack
3
How should network-device administration be protected?
A. From any user VLAN B. By shared passwords
C. Through guest Wi-Fi D. Dedicated management zone and authorized admins
Campus Network Design & Operations Workshop
45

## Slide 43
05
Building Sufficient Instrumentation
Monitoring, logging, and configuration management are part of the network architecture, not post-project extras.
Campus Network Design & Operations Workshop

## Slide 44
Instrumentation Architecture
Build a visible network from the day the first router is installed.
DATA FLOW
Core
Access
Firewall
Wireless
Collectors
SNMP • Syslog • Flow
Analytics
Dashboards • Alerts
Operations
Tickets • Action
Essential: a device is not operationally usable if you cannot see its health, configuration, and traffic behaviour

## Slide 45
What to Monitor: Minimum Operational Dataset
Collect data that answers the questions operators ask during an incident.
Reachability
Uptime, ICMP, DNS, HTTP/S, application checks
Interfaces
Up/down, throughput, errors, discards, speed/duplex, optics
Systems
CPU, memory, disk, temperature, power, fan, PoE budget
Traffic
Top talkers, source/destination, protocols, flow trends
Security
Failed logins, port violations, firewall denies, rogue DHCP/RA
Configuration
Version, startup/running config drift, backups, change audit

## Slide 46
Alert Design: Make Alerts Actionable
An alert should identify the service, severity, owner, and expected first response.
Bad alert
“Interface error.”
No device context, no trend, no owner, no urgency.
Better alert
“Core-A uplink to Library has 6% packet loss for 5 minutes.”
Includes scope and persistence.
Actionable alert
“Library uplink packet loss 6%, affecting 220 clients. Check interface errors, optics, and congestion. Escalate to campus network team.”
Alert rule: An alert is useful only when a person knows why it matters and what to do next.

## Slide 47
Inventory, Configuration Backup, and Documentation
Documentation is an operational tool. Keep it current enough to support the next incident.
Network source of truth
Device name, serial number, role, location, management IP, software, support status
Topology and addressing
Physical path, logical diagram, VLANs, subnets, routing areas, firewall zones
Configuration archive
Automated periodic backups, version history, change author, compare capability
Runbooks
Common tasks, escalation contacts, verification commands, rollback procedures
Lifecycle register
Warranty, software end-of-support, spare units, optics inventory, refresh date

## Slide 48
Operations Lab 6: Build an Instrumentation Checklist
Define the minimum data and processes needed before a new building goes live.
Device identity
Hostname, location, rack, asset tag, serial, owner, management IP
Monitoring
Reachability, interface counters, CPU/memory, optical stats, environmental data
Logging
NTP, Syslog target, auth logs, configuration change logs
Traffic visibility
Flow export from core, border, and firewall where feasible
Backup
Automated config archive and tested restore process
Documentation
Updated diagram, VLAN/subnet plan, port map, and support contact
Gate: no monitoring, no logs, no configuration backup, no production handover

## Slide 49
05
Session 05 Quiz: Instrumentation
Multiple choice • Select one answer • Part 1 of 2
1
What is the purpose of instrumentation?
A. To decorate dashboards B. To remove human review
C. To see health, configuration, and traffic behaviour D. To avoid change control
2
Which dataset records failed logins and firewall denies?
A. Reachability B. Security
C. Optical levels D. Inventory
3
What makes an alert actionable?
A. A short message only B. A device name without impact
C. A red icon D. Service, severity, owner, impact, first response
Campus Network Design & Operations Workshop
53

## Slide 50
06
Networking Roundtable
Turn the workshop into an action plan for your own campus and institution.
Campus Network Design & Operations Workshop

## Slide 51
Roundtable Case Study: The Growing Campus
Use the full framework to advise a campus that has outgrown its original flat network.
Current state
Eight buildings, unmanaged access switches, a single /16 subnet, one firewall, no central monitoring, frequent Wi-Fi complaints.
New demand
Online exams, research data transfer, dormitory Wi-Fi, public web services, more cloud applications, and new IP cameras.
Budget reality
Funding supports a phased migration. The institution needs impact first, then growth over time.
Team discussion prompts
1
What should be fixed in the first 90 days?
2
What belongs in the core, distribution, and access layers?
3
Which segments and firewall zones are essential?
4
What monitoring must exist before service expansion?
5
How would you phase equipment and fiber investments?

## Slide 52
Roundtable Output: A Phased Campus Network Plan
Present a concise plan that balances technology, budget, risk, and operations.
0-90 days
Document, segment critical services, replace unmanaged core links, establish monitoring and config backups.
3-12 months
Build core resilience, fiber hub-and-spoke paths, managed access refresh, Wi-Fi redesign, security zones.
12-24 months
Expand dual stack, automate operations, increase capacity, introduce redundancy improvements, refresh lifecycle plan.
Scoring lens: service impact, resilience gain, security improvement, operational visibility, cost, and implementation complexity.

## Slide 53
Ten Campus Network Rules to Take Back
Use these as a fast review before approving a new design or purchase.
1
Build direct, predictable backbone paths.
2
Keep major Layer 2 domains small.
3
Use routing to create clear fault and policy boundaries.
4
Place core and services where power, cooling, and physical security are strongest.
5
Use managed switches and routers in production networks.
6
Design VLANs and addressing around trust, function, and operations.
7
Protect the access edge against accidental and malicious devices.
8
Treat IPv6 as a first-class operational stack.
9
Monitor, log, backup, and document from day one.
10
Plan investment in phases, but keep the target architecture consistent.

## Slide 54
06
Session 06 Quiz: Networking Roundtable
Multiple choice • Select one answer • Part 1 of 2
1
What is the main risk in the growing campus case?
A. Too many documented diagrams B. Flat /16, unmanaged switches, no central monitoring
C. Too much IPv6 maturity D. Too many backups
2
What belongs in the first 0-90 days?
A. Document, segment critical services, replace unmanaged core links, add monitoring/backups B. Replace every endpoint
C. Build a new data centre first D. Delay all changes
3
Which 3-12 month action best supports growth?
A. Remove all VLANs B. Keep daisy-chained fibre
C. Core resilience, hub-and-spoke fibre, access refresh, Wi-Fi redesign, zones D. Disable monitoring
Campus Network Design & Operations Workshop
59

## Slide 55
06
Session 06 Quiz: Networking Roundtable
Multiple choice • Select one answer • Part 2 of 2
4
Which scoring lens should guide the phased plan?
A. Brand name only B. Port count only
C. Lowest price only D. Impact, resilience, security, visibility, cost, complexity
5
Which rule best summarizes the target architecture?
A. Keep the old flat subnet B. Design intentionally, operate visibly, improve in phases
C. Buy unmanaged switches D. Avoid documentation
Campus Network Design & Operations Workshop
60

## Slide 56
WORKSHOP CLOSE
A campus network is a service platform,
not a collection of switches.
Design it intentionally. Operate it visibly. Secure it at the right boundaries. Improve it in phases.
Discussion questions
Which campus risk causes the greatest operational pain today?
Which one design improvement would create the largest immediate benefit?
What must be monitored before the next building or service goes live?
Thank you

## Slide 57
Facilitator Answer Key
Use this slide after learners complete the section quizzes.
Session
Q1
Q2
Q3
Q4
Q5
01
Core Infrastructure Design
B
C
C
B
B
02
Equipment and Protocols
C
B
A
C
D
03
Core Network Operations
A
C
D
B
A
04
Campus Security
B
C
D
A
C
05
Instrumentation
C
B
D
A
B
06
Networking Roundtable
B
A
C
D
B
Campus Network Design & Operations Workshop
62