## Slide 1
CNDO WORKSHOP
IPv4 & IPv6 Fundamentals
Subnetting, Address Planning, and IPv6 Foundations
Mohamed Bile | CTO, SomaliREN
1

## Slide 2
SESSION OVERVIEW
What we'll cover
1
Part A — IPv4
Basics, subnetting quiz, address planning
2
Part B — IPv6, Topic 1
IPv4 exhaustion and its implications
3
Part B — IPv6, Topic 2
IPv6 address basics: notation & shortening rules
4
Part B — IPv6, Topic 3
IPv6 address types: unicast, multicast, anycast
2

## Slide 3
PART A · IPV4
IPv4 Basics
CNDO Workshop · IPv4 & IPv6 Fundamentals
3
32-bit address, written in dotted-decimal notation (e.g. 192.168.1.1)
4 octets, each ranging from 0 to 255
Every address splits into a Network portion and a Host portion
The subnet mask (or /n prefix) defines exactly where that split happens
192
8 bits
168
8 bits
1
8 bits
1
8 bits
192.168.1.1 = 32 bits total

## Slide 4
PART A · IPV4
Subnetting Recap
CNDO Workshop · IPv4 & IPv6 Fundamentals
4
CIDR notation: /n = number of network bits
2^(32-n)
Total addresses
2^(32-n) - 2
Usable hosts

## Slide 5
QUIZ 1
?
How many total IP addresses are in a /26 network?
5

## Slide 6
QUIZ 1
How many total IP addresses are in a /26 network?
A
32
B
64
C
128
D
256
CNDO Workshop · IPv4 & IPv6 Fundamentals
6

## Slide 7
QUIZ 1 · ANSWER
How many total IP addresses are in a /26 network?
A
32
✓
64
C
128
D
256
2^(32-26) = 2^6 = 64 total addresses.
7

## Slide 8
QUIZ 2
?
How many usable host addresses are in that same /26 network?
8

## Slide 9
QUIZ 2
How many usable host addresses are in that same /26 network?
A
64
B
62
C
30
D
126
CNDO Workshop · IPv4 & IPv6 Fundamentals
9

## Slide 10
QUIZ 2 · ANSWER
How many usable host addresses are in that same /26 network?
A
64
✓
62
C
30
D
126
64 total minus the network address and the broadcast address = 62 usable hosts.
10

## Slide 11
QUIZ 3
?
How many /26 subnets can you create from a single /24 network?
11

## Slide 12
QUIZ 3
How many /26 subnets can you create from a single /24 network?
A
2
B
4
C
8
D
16
CNDO Workshop · IPv4 & IPv6 Fundamentals
12

## Slide 13
QUIZ 3 · ANSWER
How many /26 subnets can you create from a single /24 network?
A
2
✓
4
C
8
D
16
A /24 borrows 2 extra bits to reach /26 -> 2^2 = 4 subnets.
13

## Slide 14
QUIZ 4
?
You have one /24 network and must create subnets for 4 departments, each needing up to 50 hosts. Which subnet mask should you use?
14

## Slide 15
QUIZ 4
You have one /24 network and must create subnets for 4 departments, each needing up to 50 hosts. Which subnet mask should you use?
A
/25
B
/26
C
/27
D
/28
CNDO Workshop · IPv4 & IPv6 Fundamentals
15

## Slide 16
QUIZ 4 · ANSWER
You have one /24 network and must create subnets for 4 departments, each needing up to 50 hosts. Which subnet mask should you use?
A
/25
✓
/26
C
/27
D
/28
/26 gives 62 usable hosts per subnet and exactly 4 subnets — the best fit for the requirement.
16

## Slide 17
PART B
IPv6 Fundamentals
1
1. IPv4 Exhaustion
Why the world had to move to IPv6
2
2. IPv6 Address Basics
Notation, format, and the two shortening rules
3
3. IPv6 Address Types
Unicast (GUA, LLA, ULA), multicast, anycast
17

## Slide 18
1
TOPIC 1 OF 3
IPv4 Exhaustion
Why the world had to move to IPv6
18

## Slide 19
TOPIC 1 · IPV4 EXHAUSTION
Global IPv4 distribution is unbalanced
CNDO Workshop · IPv4 & IPv6 Fundamentals
19
5.0
North America
0.7
Europe / Middle East
0.3
Latin America
0.2
Asia Pacific
0.1
Africa
IPv4 addresses per person, by region

## Slide 20
TOPIC 1 · IPV4 EXHAUSTION
General IPv4 pool depletion timeline
CNDO Workshop · IPv4 & IPv6 Fundamentals
20
IANA
3 Feb 2011
APNIC
19 Apr 2011
RIPE NCC
14 Sep 2012
LACNIC
10 Jun 2014
ARIN
24 Sep 2015
AFRINIC
2017

## Slide 21
TOPIC 1 · IPV4 EXHAUSTION
Exhaustion drives up address costs & NAT
CNDO Workshop · IPv4 & IPv6 Fundamentals
21
$50/address
NAT
• Network complexity
• Increase in OPEX
• Breaks end-to-end connectivity
• Cripples innovation

## Slide 22
TOPIC 1 · IPV4 EXHAUSTION
Implications for Africa: the ‘Scramble for Africa’
CNDO Workshop · IPv4 & IPv6 Fundamentals
22
1
African networks are deprived of the critical IPv4 needed to facilitate a smooth transition to IPv6
2
We are largely forced to deploy greenfield IPv6, without the dual-stack runway richer regions had
3
As a direct result, the use of NAT increases across African networks

## Slide 23
TOPIC 1 · IPV4 EXHAUSTION
Discussion: how will you deal with IPv4 exhaustion?
CNDO Workshop · IPv4 & IPv6 Fundamentals
23
Deploy IPv6
Address the root cause and future-proof the network
Deploy NAT on steroids
Squeeze more life from IPv4 with CGN and layered NAT
Wait and see
Delay the decision and hope the pressure eases

## Slide 24
2
TOPIC 2 OF 3
IPv6 Address Basics
Notation, format, and the two shortening rules
24

## Slide 25
TOPIC 2 · IPV6 ADDRESS BASICS
TCP/IP model: IPv4 vs IPv6
CNDO Workshop · IPv4 & IPv6 Fundamentals
25
IPv4 — 32 bits
ICMP
IGMP
IPSec
NAT
OSPF
IS-IS
mob. IP
IPv6 — 128 bits
ICMPv6
MLD
IPSec
ND
OSPFv3
IS-IS
mob. IP

## Slide 26
TOPIC 2 · IPV6 ADDRESS BASICS
How to write IPv6 addresses
CNDO Workshop · IPv4 & IPv6 Fundamentals
26
An IPv6 address is 128 bits long
That's 32 nibbles (4 bits each)
Written as 8 groups of 4 hex digits, separated by colons
Followed by /n for the prefix length
hhhh:hhhh:hhhh:hhhh:hhhh:hhhh:hhhh:hhhh/n
h = hexadecimal digit [0–9, a–f]
n = prefix length (decimal value)

## Slide 27
TOPIC 2 · IPV6 ADDRESS BASICS
Full IPv6 address example
CNDO Workshop · IPv4 & IPv6 Fundamentals
27
2001
4290
0010
0249
bae8
56ff
fe4a
ecfe
Each 4-hex group represents 16 bits — 8 groups × 16 bits = 128 bits total

## Slide 28
TOPIC 2 · IPV6 ADDRESS BASICS
Rules for shortening IPv6 addresses
CNDO Workshop · IPv4 & IPv6 Fundamentals
28
1
The Zero Suppression rule
Strip off all LEADING zeroes within each group.
2
The Zero Compression rule
Replace ONE contiguous run of all-zero groups with ‘::’ — usable only once per address.

## Slide 29
TOPIC 2 · IPV6 ADDRESS BASICS
Worked example: shortening an address
CNDO Workshop · IPv4 & IPv6 Fundamentals
29
2001:0000:0000:0249:0000:0000:0000:ecfe
2001:0:0:249::ecfe
Zero suppression applied to “0249” → “249”. Zero compression applied once to the trailing all-zero groups → “::”

## Slide 30
QUIZ 5
?
What does the Zero Suppression rule do?
30

## Slide 31
QUIZ 5
What does the Zero Suppression rule do?
A
Replaces contiguous all-zero groups with ::
B
Strips off leading zeroes within each group
C
Removes trailing zeroes from an address
D
Merges two IPv6 addresses together
CNDO Workshop · IPv4 & IPv6 Fundamentals
31

## Slide 32
QUIZ 5 · ANSWER
What does the Zero Suppression rule do?
A
Replaces contiguous all-zero groups with ::
✓
Strips off leading zeroes within each group
C
Removes trailing zeroes from an address
D
Merges two IPv6 addresses together
Zero Suppression only removes LEADING zeroes inside a single group (e.g. 0249 -> 249).
32

## Slide 33
QUIZ 6
?
What does the Zero Compression rule do, and how many times can it be used in one address?
33

## Slide 34
QUIZ 6
What does the Zero Compression rule do, and how many times can it be used in one address?
A
Strips leading zeroes; unlimited uses
B
Replaces one contiguous run of all-zero groups with ::, only once per address
C
Replaces every zero group with :: wherever it appears
D
It doesn't apply to IPv6 addresses
CNDO Workshop · IPv4 & IPv6 Fundamentals
34

## Slide 35
QUIZ 6 · ANSWER
What does the Zero Compression rule do, and how many times can it be used in one address?
A
Strips leading zeroes; unlimited uses
✓
Replaces one contiguous run of all-zero groups with ::, only once per address
C
Replaces every zero group with :: wherever it appears
D
It doesn't apply to IPv6 addresses
Using '::' more than once makes the number of suppressed groups ambiguous — so it is allowed only ONCE per address.
35

## Slide 36
QUIZ 7
?
Shorten this address: 2001:0DB8:0000:0000:0000:0000:1428:57ab
36

## Slide 37
QUIZ 7
Shorten this address: 2001:0DB8:0000:0000:0000:0000:1428:57ab
A
2001:DB8::1428:57ab
B
2001:0DB8::1428:57ab
C
2001:DB8:0:0:0:0:1428:57ab
D
2001::DB8::1428:57ab
CNDO Workshop · IPv4 & IPv6 Fundamentals
37

## Slide 38
QUIZ 7 · ANSWER
Shorten this address: 2001:0DB8:0000:0000:0000:0000:1428:57ab
✓
2001:DB8::1428:57ab
B
2001:0DB8::1428:57ab
C
2001:DB8:0:0:0:0:1428:57ab
D
2001::DB8::1428:57ab
Leading zero in 0DB8 is suppressed to DB8; the four contiguous zero groups compress to ::.
38

## Slide 39
QUIZ 8
?
Which of these is an INVALID shortened IPv6 address?
39

## Slide 40
QUIZ 8
Which of these is an INVALID shortened IPv6 address?
A
2001:db8::1
B
fe80::1
C
2001::db8::1
D
::1
CNDO Workshop · IPv4 & IPv6 Fundamentals
40

## Slide 41
QUIZ 8 · ANSWER
Which of these is an INVALID shortened IPv6 address?
A
2001:db8::1
B
fe80::1
✓
2001::db8::1
D
::1
2001::db8::1 uses '::' twice — invalid, since the compressed group count becomes ambiguous.
41

## Slide 42
3
TOPIC 3 OF 3
IPv6 Address Types
Unicast (GUA, LLA, ULA), multicast, and anycast
42

## Slide 43
TOPIC 3 · IPV6 ADDRESS TYPES
There are 3 types of IPv6 addresses
CNDO Workshop · IPv4 & IPv6 Fundamentals
43
U
Unicast
1 : 1 — delivered to exactly one interface
M
Multicast
1 : n — delivered to every member of a group
A
Anycast
1 : closest — delivered to the nearest interface
Note: there is no broadcast address (or broadcast communication) in IPv6

## Slide 44
TOPIC 3 · IPV6 ADDRESS TYPES
An address has scope = extent of uniqueness
CNDO Workshop · IPv4 & IPv6 Fundamentals
44
G
Global scope
Unique across the entire internet
L
Link-local scope
Unique only within the local link/segment
Within a scope, an address can be used as a unique ID for an interface

## Slide 45
TOPIC 3 · IPV6 ADDRESS TYPES
Global Unicast Addresses (GUA)
CNDO Workshop · IPv4 & IPv6 Fundamentals
45
001
3 bits
Global Routing Prefix
n bits
SubnetID
64-n bits
InterfaceID
64 bits
2001:4290:10:249:bae8:56ff:fe4a:ecfe (prefix range 2000::/3)

## Slide 46
TOPIC 3 · IPV6 ADDRESS TYPES
Link-Local Addresses (LLA)
CNDO Workshop · IPv4 & IPv6 Fundamentals
46
1111111010
10 bits
0
54 bits
InterfaceID
64 bits
fe80:0000:0000:0000:bae8:56ff:fe4a:ecfe (prefix fe80::/10)

## Slide 47
TOPIC 3 · IPV6 ADDRESS TYPES
Link-local reachability and ScopeID
CNDO Workshop · IPv4 & IPv6 Fundamentals
47
Every interface can have the same fe80:: prefix — it's only unique per link
A router with multiple links doesn't know which interface to send a link-local packet out of
You must additionally specify the egress interface
ping fe80::1 → which interface does the router send it out of?

## Slide 48
TOPIC 3 · IPV6 ADDRESS TYPES
Unique Local Addresses (ULA)
CNDO Workshop · IPv4 & IPv6 Fundamentals
49
1111 110L
8 bits
SubnetID (0)
56 bits
InterfaceID
64 bits
fc00::/7 — L=0 unassigned, L=1 → fd00::/8 (free-use self-assignment)

## Slide 49
TOPIC 3 · IPV6 ADDRESS TYPES
Generating the InterfaceID (IID)
CNDO Workshop · IPv4 & IPv6 Fundamentals
50
1
Static
Manually configured
Servers, router interfaces
2
EUI-64
Derived from the MAC address
Automatically configured hosts
3
Cryptographic
Derived using cryptographic functions
Automatically configured hosts
4
Pseudo-random
Randomly generated, changes over time
Automatically configured hosts

## Slide 50
TOPIC 3 · IPV6 ADDRESS TYPES
How EUI-64 InterfaceIDs are generated
CNDO Workshop · IPv4 & IPv6 Fundamentals
51
1
MAC address (48 bits)
00:90:27:17:FC:0F
2
Insert FFFE at the midpoint (→ 64 bits)
00:90:27:FF:FE:17:FC:0F
3
Flip the U/L bit (unique MAC → 0→1 in 7th bit)
02:90:27:FF:FE:17:FC:0F

## Slide 51
TOPIC 3 · IPV6 ADDRESS TYPES
Important well-known addresses
CNDO Workshop · IPv4 & IPv6 Fundamentals
52
::
Unspecified address — host has no IPv6 address; never used as a destination
::/0
Represents all IPv6 addresses (default route)
::1
IPv6 loopback address — must never be forwarded outside the node

## Slide 52
TOPIC 3 · IPV6 ADDRESS TYPES
Anycast addresses
CNDO Workshop · IPv4 & IPv6 Fundamentals
53
The same unicast address is assigned to multiple interfaces
Anycast packets are delivered to the topologically closest interface holding that address
Anycast packets reach the nearest green node, not all of them

## Slide 53
TOPIC 3 · IPV6 ADDRESS TYPES
Multicast addresses
CNDO Workshop · IPv4 & IPv6 Fundamentals
54
11111111
8 bits
flags
4b
scope
4b
network prefix
64 bits
groupID
32 bits
All multicast addresses fall in the range ff00::/8

## Slide 54
TOPIC 3 · IPV6 ADDRESS TYPES
Well-known multicast scopes
CNDO Workshop · IPv4 & IPv6 Fundamentals
55
Bits
Hex
Scope
0001
1
Interface-local
0010
2
Link-local
0100
4
Admin-local
0101
5
Site-local
1000
8
Organization-local
1110
e
Global

## Slide 55
QUIZ 9
?
How many types of IPv6 addresses are there?
56

## Slide 56
QUIZ 9
How many types of IPv6 addresses are there?
A
2 — Unicast, Multicast
B
3 — Unicast, Multicast, Anycast
C
4 — including Broadcast
D
5
CNDO Workshop · IPv4 & IPv6 Fundamentals
57

## Slide 57
QUIZ 9 · ANSWER
How many types of IPv6 addresses are there?
A
2 — Unicast, Multicast
✓
3 — Unicast, Multicast, Anycast
C
4 — including Broadcast
D
5
IPv6 has exactly 3 address types. There is no broadcast address in IPv6.
58

## Slide 58
QUIZ 10
?
True or False: IPv6 still supports broadcast addresses like IPv4.
59

## Slide 59
QUIZ 10
True or False: IPv6 still supports broadcast addresses like IPv4.
A
True
B
False
CNDO Workshop · IPv4 & IPv6 Fundamentals
60

## Slide 60
QUIZ 10 · ANSWER
True or False: IPv6 still supports broadcast addresses like IPv4.
A
True
✓
False
False — multicast addresses replace the role broadcast played in IPv4.
61

## Slide 61
QUIZ 11
?
What is the prefix range for Global Unicast Addresses (GUA)?
62

## Slide 62
QUIZ 11
What is the prefix range for Global Unicast Addresses (GUA)?
A
fe80::/10
B
fc00::/7
C
2000::/3
D
ff00::/8
CNDO Workshop · IPv4 & IPv6 Fundamentals
63

## Slide 63
QUIZ 11 · ANSWER
What is the prefix range for Global Unicast Addresses (GUA)?
A
fe80::/10
B
fc00::/7
✓
2000::/3
D
ff00::/8
Global Unicast Addresses fall in the 2000::/3 range.
64

## Slide 64
QUIZ 12
?
What is the prefix for Link-Local Addresses (LLA)?
65

## Slide 65
QUIZ 12
What is the prefix for Link-Local Addresses (LLA)?
A
2000::/3
B
fe80::/10
C
fc00::/7
D
::1/128
CNDO Workshop · IPv4 & IPv6 Fundamentals
66

## Slide 66
QUIZ 12 · ANSWER
What is the prefix for Link-Local Addresses (LLA)?
A
2000::/3
✓
fe80::/10
C
fc00::/7
D
::1/128
Link-Local Addresses always begin with fe80::/10.
67

## Slide 67
QUIZ 13
?
What is the prefix range for Unique Local Addresses (ULA)?
68

## Slide 68
QUIZ 13
What is the prefix range for Unique Local Addresses (ULA)?
A
fe80::/10
B
fc00::/7
C
2000::/3
D
ff00::/8
CNDO Workshop · IPv4 & IPv6 Fundamentals
69

## Slide 69
QUIZ 13 · ANSWER
What is the prefix range for Unique Local Addresses (ULA)?
A
fe80::/10
✓
fc00::/7
C
2000::/3
D
ff00::/8
ULAs use the fc00::/7 range (fd00::/8 in practice, for free-use self-assignment).
70

## Slide 70
QUIZ 14
?
Which prefix range is used for IPv6 multicast traffic?
71

## Slide 71
QUIZ 14
Which prefix range is used for IPv6 multicast traffic?
A
2000::/3
B
fe80::/10
C
ff00::/8
D
fc00::/7
CNDO Workshop · IPv4 & IPv6 Fundamentals
72

## Slide 72
QUIZ 14 · ANSWER
Which prefix range is used for IPv6 multicast traffic?
A
2000::/3
B
fe80::/10
✓
ff00::/8
D
fc00::/7
All multicast addresses fall within ff00::/8.
73

## Slide 73
QUIZ 15
?
What does the address ::1 represent?
74

## Slide 74
QUIZ 15
What does the address ::1 represent?
A
All IPv6 addresses
B
A host with no address
C
The loopback interface (like 127.0.0.1 in IPv4)
D
The global unicast prefix
CNDO Workshop · IPv4 & IPv6 Fundamentals
75

## Slide 75
QUIZ 15 · ANSWER
What does the address ::1 represent?
A
All IPv6 addresses
B
A host with no address
✓
The loopback interface (like 127.0.0.1 in IPv4)
D
The global unicast prefix
::1 is the IPv6 loopback address and must never be forwarded outside the node.
76

## Slide 76
QUIZ 16
?
Which of the following is a valid method for generating an Interface ID (IID)?
77

## Slide 77
QUIZ 16
Which of the following is a valid method for generating an Interface ID (IID)?
A
EUI-64
B
Static / manual
C
Pseudo-random
D
All of the above
CNDO Workshop · IPv4 & IPv6 Fundamentals
78

## Slide 78
QUIZ 16 · ANSWER
Which of the following is a valid method for generating an Interface ID (IID)?
A
EUI-64
B
Static / manual
C
Pseudo-random
✓
All of the above
All four methods — static, EUI-64, cryptographic, and pseudo-random — are valid ways to generate an IID.
79

## Slide 79
Questions?
Thank you — CNDO Workshop · SomaliREN
83